■ FEATURES

● 20A (A-contact), 15A (B-Contact).

● Subminiature.

● Standard PC Layout.

■ CONTACT DATA

| Contact Form | 1A, 1C |
| --- | --- |
| Contact Material | Ag Alloy |
| Contact Ratings | 20A 14VDC(1 Form A), 15A 14VDC(1 Form B) |
| Max Switching Voltage | 28VDC |
| Max Switching Current | Flasher | 30A / Inrush 40A |
|  | Motor load | 15A 14VDC Inrush 20A |
| Max Switching Power | 500W |
| Contact Resistance | 100mΩ Max (Initial Value) |
| Life Expectancy | Electrical | 100,000operations at 30 operations / minute) |
|  | Mechanical | 10,000,000 operations |

■ GENERAL DATA

| Insulation Resistance | 100M Ω Min. at 500VDC |
| --- | --- |
| Dielectric Strength | Open Contacts | 500VAC (For one minute) |
|  | Contacts and Coil | 1,500VAC (For one minute) |
| Operate Time | 15ms |
| Release Time | 10ms |
| Temperature Range | Operating | -40℃ ~ 85℃ |
|  | Storage | -40℃ ~ 95℃ |
| Shock Resistance | Operate Extremes | 10G |
|  | Damage Limits | 100G |
| Vibration Resistance | 10 ~ 50Hz 1.5mm |
| Humidity | 40 ~ 85% |
| Weight | Approx 10g |

■ ORDERING INFORMATION

■ COIL DATA

| Nominal Voltage (VDC) | Rated current ±10% at 25°C ( mA ) | Coil Resistance ±10% at 25°C ( Ω ) | Max Operating Voltage VDC | Min Release Voltage VDC | Max continuous Voltage at 25°C | Power consumption At rated Voltage |
| --- | --- | --- | --- | --- | --- | --- |
| 9 | 71.4 | 126 | 5.85 | 0.45 | 10.8 | Approx. 0.64W |
| 12 | 53.3 | 225 | 7.8 | 0.6 | 14.4 |  |
| 24 | 26.7 | 900 | 15.6 | 1.2 | 28.8 |  |
| 6 | 133.3 | 45 | 3.9 | 0.3 | 7.2 | Approx. 0.8W |
| 12 | 66.6 | 180 | 7.8 | 0.6 | 14.4 |  |
| 24 | 33.3 | 720 | 15.6 | 1.2 | 28.8 |  |

■ OVERALL AND MOUNTING DIMENSIONS

# Text boxes

#### RE1