| RM2, RM2A Relays |  |
| --- | --- |
| Lamp load 2(4) x 21W Flashing frequency : 70 to 90 cycles / minute Lamp outage frequency : 120 to 230 (c/min) Dustproof structure |  |

CHARACTERISTICS

| Norminal Voltage | 12 VDC |
| --- | --- |
| Contact Rating | Lamp Load : 2(4) x 21W |
| Ambient temperature | -30°C to 70°C |
| Oscillation frequency | 70 to 90 cycles / minute |
| Lamp outage frequency | 120 to 230 (c/min) |
| Duty cycle | 35% to 70% |
| Weight | Approx. 40g |
| Terminal type | QC |
| Outline LxWxH | 30 x 30 x 40mm |
| Load Voltage Range | 9 to 15VDC |
| Oscillation | 10 to 55Hz 49m/s2(5g) |
| Impulsion | 200m/s2(20g) |
| Electrical Life | 100h | Lamp Load 2x21W |
|  | 36h | Lamp Load 4x21W |

- As shown in left wiring diagram, terminal B is connected with anode of 12VDC, terminal E with cathode, and terminal L with lamp load.

- When the lamp load is 2× 21W + 5W or 4 ×21W + 2×5W, the relay will control lamp flashing with the frequency (65 to 95) times / minute.

- When the lamp load is 1×21W + 5W (one 21W lamp fails), the relay will control lamp flashing with the frequency (150 to 190) times / minute.

OUTLINE DIMENSIONS AND WIRING DIAGRAM