HANDOUK

►FEATURE

● General Purpose power relay

● 35mm DIN rail for plug-in socket

● UL,cUL,CQC approved

● LED and Diode can be installed

● Various sockets available

►PRODUCT PROPERTIES                      Size : (L x W x H) 28 x 21.5 x 36mm

| Contact Form | 2C | 3C | 4C |
| --- | --- | --- | --- |
| Contact Material | Ag alloy |
| Contact Ratings | 5A, 240VAC / 28VDC | 3A, 240VAC / 28VDC |
| Max Switching Power | 1,200VA / 140W | 720VA / 140W |
| Contact Resistance | 100mΩMax at 6VDC 1A | 50mΩMax at 6VDC 1A |
| Life Expectancy | Electrical | 100,000 Operations (at 30 Operations / minute) |
|  | Mechanical | 10,000,000 Operations |
| Pick-up voltage (At 25°C) | DC : ≤ 75 % Un., AC : ≤ 80 % Un. |
| Drop-out voltage (At 25°C) | DC : ≥10 % Un., AC : ≥ 30 % Un. |
| Max. allowable coil voltage | 120 % Un. (At 25 ºC) |
| Insulation Resistance | 500MΩ Min. at 500VDC |
| Dielectric Strength Between | Open Contacts | 1,000VAC(for one minute) (Leak current : 1mA) |
|  | Contact poles | 1,000VAC(for one minute) (Leak current : 1mA) |
|  | Contacts and coil | 1,500VAC(for one minute) (Leak current : 1mA) |
| Operate Time | 15ms |
| Release Time | 10ms |
| Nominal coil power | DC(W) | 0.9 |
|  | AC(VA) | 1.2 |
| Temperature Range | -55ºC ~ +70ºC |
| Humidity | 35% - 85% RH |
| Atmospheric | 86~106KPa |
| Shock Resistance | 10G (Malfunction) |
| Vibration Resistance | 10-55Hz,1.0mm |
| Weight | Approx 35g |
| Safety Standard | E197546 |

►COIL PARAMETER

| Rated Voltage | Pick-up Voltage(Max) | Drop-out Voltage(Min) | Coil Resistance (Ω)+/-10% | Nominal Power | Max. V allowable |
| --- | --- | --- | --- | --- | --- |
| 12VDC | 9VDC | 1.2VDC | 160Ω | 0.9W | 110% of nominal voltage |
| 24VDC | 18VDC | 2.4VDC | 640Ω |  |  |
| 48VDC | 36VDC | 4.8VDC | 2,560Ω |  |  |
| 110VDC | 82.5VDC | 11VDC | 133,450Ω |  |  |
| 12VAC | 9.6VAC | 3.6VAC | 42Ω | 1.2VA |  |
| 24VAC | 19.2VAC | 7.2VAC | 168Ω |  |  |
| 48VAC | 38.4VAC | 14.4VAC | 672Ω |  |  |
| 220VAC | 176VAC | 66VAC | 14,100Ω |  |  |

►ORDERING INFORMATION

►DIMENSIONS  (Unit: mm)

# Text boxes

#### GA