HANDOUK

►FEATURES

- 60A Surge current capability

- 2 pole configuration for surge current switching.

- Quick connect terminals

- 12.7mm creepage distance between coil and contact

►CONTACT  DATA

| Contact Form | 2A / 2B / 2C |
| --- | --- |
| Initial Contact Resistance | ≤ 100mΩ (at 24Vd.c. 1A) |
| Contact Material | Ag alloy |
| Contact Ratings | 15A 277VAC 12A 125VAC (Resistive Load) |
| Max. Switching Voltage | 277VAC |
| Max. Switching Current | 15A |
| Max. Switching Power | 4,155VA |
| Mechanical life | 7.5 ⅹ105 OPS |
| Electrical life | 1 ⅹ105 OPS |

►CHARACTERISTICS

| Insulation Resistance | ≥100MΩ (500Vd.c.) |
| --- | --- |
| Dielectric Strength Between | Open Contacts: | 750Vrms 1 min |
|  | Coil To Contacts: | 2,500Vrms 1 min |
| Coil Temperature rise (60Hz Rated Voltage) | Max. 50℃ |
| Shock Resistance | Functional | 98m/s2 (10g) |
|  | Destructive | 490m/s2 (50g) |
| Vibration Resistance | 1.0mm 10Hz~55Hz |
| Humidity Range | 35%~85% RH |
| Temperature Range | -40℃~70℃ |
| Sealed method | Dust protected |

►COIL DATA

| Nominal Voltage (VAC) | Pick-up Voltage (≤) VAC | Drop-out Voltage (≤) VAC | Rated coil Current mA (at 20℃) | Coil Resistance at 20℃ Ω ± 20% |
| --- | --- | --- | --- | --- |
|  | Standard | Extreme | Standard | Extreme |  |  |
| 24 | 19.2 | 21 | 4.8 | 3.6 | 417 | 17.8 |
| 120 | 96 | 105 | 24 | 18 | 83 | 420 |
| 208/240 | 166.4 | 183 | 41.6 | 31.2 | 41.7 | 1,600 |

►ORDERING INFORMATION

GF1      -2c      - 120AC

►OUTLINE DIMENSIONS  (Unit: MM)

Disclaimer

This datasheet is for the customers’ reference. All the specifications are subject to change without notice.

# Text boxes

#### GF1

COIL VOLTAGE

24VAC

120VAC

240VAC

CONTACT FORM

2A：2 Form A

2B：2 Form B

2C：2 Form C

MODEL