Handouk

►FEATURES

- Class F coil insulation system for 155℃ temperature

- Coil molded in PET for environmental protection

- Rugged construction rivets terminals to base

- 30A and 50Amp heavy duty power relay

►CONTACT  DATA

| Contact Form | Short base:1A, 1B, 1X, 1C, 2A Long base:1Y, 2B, 2C |
| --- | --- |
| Initial Contact Resistance | Max: 100mΩ |
| Contact Material | Silver Alloy Plate Silver |
| Type GF2 | UL Ratings |
|  | 30AMP 1-1/2HP 120/240VAC 2HP 240VAC 20AMP 600VAC 30AMP 28VDC |
| GF2R GF2D GF2W | Same as GF2 with addition 50A 277VDC Same as GF2 with addition 20A 125VDC Same as GF2 with addition of Auxiliary 1/4HP at 125/250VAC |
| Max. Switching Voltage | 600VAC/125VDC |
| Max. Switching Current | 50A |
| Max. Switching Power | 7200VA 2500W |
| Mechanical life | 1ⅹ106 OPS |
| Electrical life | 1ⅹ105 OPS |

►CHARACTERISTICS

| Insulation Resistance | 1000MΩ (500VDC) |
| --- | --- |
| Dielectric Strength Between Contacts: | 2200Vrms 1 minute |
| Between Other Elements: | 2200Vrms 1 minute |
| Operate time | ≤30ms |
| Release Time | ≤30ms |
| Coil Temperature Rise | AC: ≤ 70℃ (60HZ) DC: ≤ 45℃ |
| Operating Ambient | AC: -45℃-85℃ (30A) -45℃-70℃（50A） DC: -45℃-105℃ |
| Shock resistance | Functional | 98m/s2 (10g) |
|  | Destructive | 980m/s2(100g) |
| Vibration resistance | 1.5mm 10 to 55HZ |
| Humidity | 35% to 85% RH |
| Unit weight | Long base: ≤285g Short base: ≤230g |

►Coil

| Nominal coil power | 9.5VA, 2W |
| --- | --- |
| Nominal Voltage | 6~480VAC, 6~110VDC |

Notes: The data shown above don’t include the power of electronic indicating circuit when the relay picks-up.

►COIL DATA

| Nominal Voltage (VDC) | Pick-up Voltage (≤) VDC | Drop-out Voltage (≤) VDC | Coil Resistance at 25℃ Ω ± 10% |
| --- | --- | --- | --- |
| 6 | 4.5 | 0.6 | 18 |
| 12 | 9 | 1.2 | 72 |
| 24 | 18 | 2.4 | 290 |
| 36 | 27 | 3.6 | 650 |
| 48 | 36 | 4.8 | 1,150 |
| 110 | 82.5 | 11 | 6,050 |
| Nominal Voltage (VAC) | Pick-up Voltage (≤) VAC | Drop-out Voltage (≤) VAC | Coil Resistance at 25℃ Ω ± 10% |
| 12 | 10.2 | 3.6 | 2.85 |
| 24 | 20.4 | 7.2 | 11.5 |
| 48 | 40.8 | 14.5 | 48 |
| 120 | 102 | 35 | 295 |
| 208 | 177 | 62 | 845 |
| 240 | 204 | 70 | 1,170 |
| 277 | 236 | 83 | 1,655 |
| 480 | 408 | 140 | 4,860 |

►ORDERING INFORMATION

GF2    R      Q     W     /120     A     -2C

Basic  Designation

Contact  rating：

R： 50A  250VAC

D:：20A  125VDC

Nil：30A  250vac

Terminal  Type：

Q：QC coil Terminals

Nil： Screw Terminals

Microswitch：

Nil： Without microswitch

W： With microswitch

Coil Voltage： 6~480VAC； 6~110VDC

Coil Current：A： AC： D： DC

1A：1 Form A；1B：1 Form B；1C：1 Form C；1X：1 Form X；

1Y：1 Form Y；2A：2 Form A；2B：2 Form B；2C：2 Form C

►OUTLINE DIMENSIONS  (Unit: MM)

Disclaimer

This datasheet is for the customers’ reference. All the specifications are subject to change without notice.

# Text boxes

#### GF2