| · Contact Form : 1 Form C, 2 Form C · High contact load : 30A · High reliability |  |
| --- | --- |

►contact dATA

| Contact Form | 1A,1B,1C 2A,2B,2C |
| --- | --- |
| Initial Contact Resistance | 50mΩ(at 1A 24VDC) |
| Contact Material | Silver Alloy |
| Contact Ratings | 20A/30A 250VAC/30VDC 18A 380VAC, 16A 440VAC |
| Max. switching voltage | 48VDC/440VAC |
| ►Coil Data |
| Insulation Resistance | Min. 500MΩ 500VDC |
| Operate Time | Max. 20msec |
| Release Time | Max. 15msec |
| Dielectric Strength Between | Open Contacts | 1,500VAC 1min |
|  | Contacts and coil | 2,500VAC 1min |
| Terminal Type | Plug-in, Flange |

►COIL Data

vdc

| Nominal Voltage VDC | Pick-up Voltage VDC | Drop-out Voltage VDC | Standard Coil Resistance at 20℃ |
| --- | --- | --- | --- |
| 6 | 4.5 | 0.6 | 18±10% |
| 9 | 6.75 | 0.9 | 40.5±10% |
| 12 | 9 | 1.2 | 72±10% |
| 18 | 13.5 | 1.8 | 162±10% |
| 24 | 18 | 2.4 | 288±10% |
| 48 | 36 | 4.8 | 1,125±10% |
| 60 | 45 | 6 | 1,800±10% |
| 110 | 82.5 | 11 | 6,050±10% |
| VAC |
| Nominal Voltage VAC | Pick-up Voltage VAC | Drop-out Voltage VAC | Coil Resistance |
| 6 | 4.8 | 1.8 | 3.15±10% |
| 9 | 7.2 | 2.7 | 7.1±10% |
| 12 | 9.6 | 3.6 | 12.6±10% |
| 18 | 14.4 | 5.4 | 28.4±10% |
| 24 | 19 | 7.2 | 50.4±10% |
| 48 | 38.4 | 14.4 | 113±10% |
| 110 | 88 | 33 | 1,100±10% |
| 220 | 176 | 66 | 4,200±10% |

►Ordering Code

Overall and mounting dimensions

useful curve

# Text boxes

#### GW RELAY