HANDOUK

■ FEATURES

● 12A switching capability

● 1 Form A and 1 Form C contact arrangement

● Sealed & Unsealed types available

● 2kV dielectric strength between coil and contacts

● Outline Dimensions : 22.5 x 16.5 x 16.5mm

■ CONTACT DATA

| Contact Form | 1A | 1C |
| --- | --- | --- |
| Contact Material | AgCdO, AgSnO2 |
| Contact Ratings | 10A 250VAC | 12A 125VAC NO : 10A 250VAC NC : 7A 250VAC |
| Max Switching Voltage | 250VAC / 30VDC |
| Max Switching Current | 12A |
| Max Switching Power | Max. 2,500VA / 300W | Max. 2,500VA / 210W |
| Contact Resistance | 100mΩ Max at 6VDC 1A |
| UL/CUR rating | 10A, 277VAC 10A 28VDC | 12A, 125VAC 7A 277VAC /28VDC |
| Life Expectancy | Electrical | 100,000operations (at 30operations/minute) |
|  | Mechanical | 10,000,000operations |

■ GENERAL DATA

| Insulation Resistance | 100M Ω Min. at 500VDC |
| --- | --- |
| Dielectric Strength | Open Contacts | 750VAC (For one minute) |
|  | Contacts and Coil | 2,000VAC (For one minute) |
| Operate Time | 10ms |
| Release Time | 5ms |
| Temperature Range | -40℃ ~ 85℃ |
| Shock Resistance | Operate Extremes | 10G |
|  | Damage Limits | 100G |
| Vibration Resistance | 10 ~ 50Hz 1.5mm |
| Humidity | 35 ~ 85% |
| Dimensions(mm) | 22.5 x 16.5 x 16.5 |
| Weight | Approx 14g |
| Safety Standard | UL222977 |

■ COIL DATA

| Nominal Voltage (VDC) | Coil Resistance | Max Operating Voltage VDC | Min Release Voltage VDC | Max Applicable Voltage VDC |
| --- | --- | --- | --- | --- |
|  | 0.36W |  |  |  |
| 3 | 25Ω | 2.3 | 0.3 | 3.9 |
| 5 | 70Ω | 3.8 | 0.5 | 6.5 |
| 6 | 100Ω | 4.5 | 0.6 | 7.8 |
| 9 | 225Ω | 6.8 | 0.9 | 11.7 |
| 12 | 400Ω | 9 | 1.2 | 15.6 |
| 18 | 900 | 13.5 | 1.8 | 23.4 |
| 24 | 1,600Ω±15% | 18 | 2.4 | 31.2 |
| 48 | 6,400Ω±15% | 36 | 4.8 | 62.4 |

■ ORDERING INFORMATION

■ USEFUL CURVES

■ OVERALL AND MOUNTING DIMENSIONS

# Text boxes

#### HA2D