HANDOUK

►FEATURES

● 10A Switching capabilities.

● SPST configurations.

● Subminiature, PCB layout

● Sealed and unsealed type available

Size (L x W x H)

18.8 x 10.6 x 15.6mm

►CONTACT DATA

| Contact Form | 1 Form A (SPST) | 1 Form C (SPDT) |
| --- | --- | --- |
| Contact Ratings | Standard | High Capacity | 3A 240VAC 3A 30VDC |
|  | 10A 120VAC 5A 240VAC 5A 30VDC | 10A 250VAC 10A 240VAC |  |
| Contact Material | Silver Alloy |
| Max. Switching Voltage | 250VAC / 30VDC |
| Max. Switching Current | 10A |
| Max. Switching Power | 1,200VA/150W |
| Contact Resistance | 100mΩ Max at 24VDC 1A |
| Life Expectancy | Electrical | 100,000 Operations (at 30 ops a minute) |
|  | Mechanical | 10,000,000 Operations |

►OPERATION CONDITION

| Insulation Resistance | 100MΩ min (at 500VDC) |
| --- | --- |
| Dielectric Strangth | Between open Contacts | 750VAC (For one minute) |
|  | Between coil & Contacts | 2,500VAC (For one minute) |
| Operate time | 8ms |
| Release Time | 5ms |
| Shock resistance | Operating Extremes | 10G |
|  | Damage Limits | 100G |
| Vibration resistance | 10~55Hz Double amplitude |
| Humidity | 35~95% |
| Temperature Range | -40 ~ 70℃ |
| Weight | Approx 6g |
| Safety Standard (UL) | cULus | E197546 |
|  | TUV | R50162334 |

►COIL PARAMETER

| Nominal Voltage (VDC) | Coil Resistance at 20 C (Ω) | Max Operate Voltage | Min. Release Voltage | Max. Applicable Voltage |
| --- | --- | --- | --- | --- |
|  | Standard | Sensitive |  |  |  |
| 3 | 20 +/-10% | 45 +/-10% | 2.25 | 0.15 | 3.9 |
| 5 | 55 +/-10% | 125 +/-10% | 3.75 | 0.25 | 6.5 |
| 6 | 80 +/-10% | 180 +/-10% | 4.50 | 0.30 | 7.8 |
| 9 | 180 +/-10% | 400 +/-10% | 6.75 | 0.45 | 11.7 |
| 12 | 320 +/-10% | 720 +/-10% | 9.00 | 0.60 | 15.6 |
| 18 | 720 +/-10% | 1600 +/-10% | 13.5 | 0.90 | 23.4 |
| 24 | 1280 +/-10% | 2800 +/-10% | 18.0 | 1.20 | 31.2 |

►ORDERING INFORMATION

►DIMENSIONS  (Unit: MM)

# Text boxes

#### HE