HANDOUK

| ■ FEATURES ● 1 Form A or 1 Form C ● Standard and Sensitive Coils ● Sealed and Unsealed Type Available ● UL / CUR Approved E197546 |  |
| --- | --- |

■ CONTACT DATA                               ■ GENERAL DATA

| Contact Form | 1 Form A | 1 Form C |
| --- | --- | --- |
| Contact resistance Max. (At 1A 6VDC) | 100 mΩ |
| Contact Material | Silver Alloy |
| Contact Rating (Res. Load) | 5A 250VAC 5A 3VDC | Standard | High power |
|  |  | N.C. 3A N.O. 5A | N.C. 5A N.O. 5A |
| Switching Voltage | 250VAC / 30VDC (Max) |
| Switching Current | 5A |
| Max.Switching Power | 1250VA | 1250VA(N0) 750VA(NC) | 1250VA |
| Electrical Life | 100,000operations (At 30 operations / minute) |
| Mechanical Life | 10,000,000 operations |
| Insulation Resistance | 1000M Ω Min. at 500VDC |
| Dielectric Strength | Open Contacts | 1,000VAC (For one minute) |
|  | Contacts and Coil | 2,000VAC (For one minute) |
| Surge Voltage between contacts and coil | 4,000VAC (At 2 x 10 micro sec) |
| Operate Time | 10ms |
| Release Time | 5ms |
| Temperature Rise | Max. 55℃ |
| Ambient Temperature | -40 ~ 85℃ |
| Shock Resistance | 100m/s2 |
| Vibration Resistance | 10 ~ 55Hz 10g, Amplitude of 3.3mm |
| Humidity | 45 ~ 85% |
| Dimension | 20.5 x 20.5 x 10.5mm |
| Weight | Approx. 8g |
| Construction | Sealed and unsealed |

■ COIL DATA

| Coil Consumption | 0.36W, 0.25W |
| --- | --- |
| Coil Voltage | 3 ~ 48 VDC |
| Coil Resistance | See below table |

■ TABLE

| Nominal Voltage VDC | Pick-up Voltage VDC | Drop-out Voltage VDC | Coil Current mA | Coil Resistance Ω | Pick-up Voltage VDC | Drop-out Voltage VDC | Coil Current mA | Coil Resistance Ω |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
|  | Standard Coil, 0.36W | Sensitive Coil, 0.25W |
| 3 | 2.1 | 0.15 | 12 | 25±10% | 2.2 | 0.15 | 8.3 | 36±10% |
| 5 | 3.5 | 0.25 | 72 | 69±10% | 3.6 | 0.25 | 50 | 100±10% |
| 6 | 4.2 | 0.3 | 60 | 100±10% | 4.3 | 0.3 | 41 | 145±10% |
| 9 | 6.3 | 0.45 | 40 | 225±10% | 6.5 | 0.45 | 28 | 325±10% |
| 12 | 8.4 | 0.6 | 30 | 400±10% | 8.6 | 0.6 | 21 | 575±10% |
| 18 | 12.6 | 0.9 | 20 | 900±10% | 13 | 0.9 | 14 | 1300±10% |
| 24 | 16.8 | 1.2 | 15 | 1600±10% | 17.3 | 1.2 | 10 | 2310±10% |
| 48 | 33.6 | 2.4 | 7.5 | 6400±10% | 34.6 | 2.4 | 5 | 9220±10% |

| HG | Model Name |
| --- | --- |
| 1A | 1A: SPST, 1C: SPDT |
| T | T: High Power, Nil: Standard |
| 12 | Coil Voltages : 3, 5, 6, 9, 12, 18, 24, 48Vdc |
| S | S: Sealed type, Nil: Standard type |
| H | H: Sensitive type, Nil: Standard type |

■ ORDERING INFORMATION

ex) HG-1AT-12SH

※ Additional "(555)" for RoHs products

 and contact material AgSnO2
 "(554)" for RoHs products and contact

 material AgNi

■ OVERALL AND MOUNTING DIMENSIONS

■ USEFUL CURVE

Handouk Electronics Co., Ltd                                             E-mail : sales@handouk.co.kr

# Text boxes

#### HG Relay