HANDOUK

| ■ FEATURES ● 16A switching capabilities ● Latching relay ● Capacitor load up to 200μF (Min. inrush current at 500A/10μs) ● Min. inrush current Capa 170A | ● Environmental Friendly product (RoHs compliant) ● Outline Dimensions: (29.0 x 13.0 x 15.7)mm |  |
| --- | --- | --- |

■ CONTACT DATA                             ■ GENERAL DATA

| Contact Form | 1A, IB, 1C |
| --- | --- |
| Contact Material | AgSnO2, W+ AgSnO2 |
| Contact Rating | 1A, 1B: 16A 250VAC, 1x105 ops(Resistive) 20A 250VAC, 3 x104 ops(Resistive) 1.5HP 240VAC(Motor) 8A 220VAC cosØ=0.4, 1x105ops(Inductive) 1AT(W+AgSnO2)3,000W220VAC 1.5x104ops (Incandescent &fluorescent lamp) 1C: 16A 250VAC, 5x104ops |
| Max.Switching Voltage | 277VAC |
| Max. Contact current | 16A |
| Max. Switching Power | 5,000VA |
| Electrical Life | See “Contact Rating” |
| Mechanical Life | 3,000,000 operations |

| Insulation Resistance | 1,000M Ω Min. at 500VDC |
| --- | --- |
| Dielectric Strength | Open Contacts | 1,000VAC (For one minute) |
|  | Contacts and Coil | 4,400VAC (For one minute) |
| Creepage distance | 8mm |
| Operate Time | 15ms |
| Release Time | 15ms |
| Temperature Range | -40℃ ~ 85℃ |
| Shock Resistance | 98m/s2 |
| Vibration Resistance | 10Hz to 55Hz 1.5mm DA |
| Humidity | 5 ~ 85% RH, 40℃ |
| UL Approval | E222977 |
| Termination | PCB |
| Weight | Approx. 13g |
| Construction | Plastic Sealed & Flux proofed |

■ COIL DATA

| Coil Power |
| --- |
| One Coil Latching | 400mW |
| Two Coil Latching | 600mW |

■ TABLE                                                                                      ( at 20℃ )

| Nominal Voltage VDC | Pick-up Voltage VDC | Coil Current mA | Coil Resistance ohm | Pick-up Voltage VDC | Coil Current mA | Coil Resistance ohm±10% |
| --- | --- | --- | --- | --- | --- | --- |
| One Coil Latching, 0.4W | Two Coil Latching, 0.6W |
| 3 | 2.4 | 130 | 22.5±10% | 2.4 | 200 | 15+15 |
| 5 | 4.0 | 80 | 62.5±10% | 4.0 | 119 | 42+42 |
| 6 | 4.8 | 66.6 | 90±10% | 4.8 | 100 | 60+60 |
| 12 | 9.6 | 33.3 | 360±10% | 9.6 | 50 | 240+240 |
| 24 | 19.2 | 16.6 | 1,440±10% | 19.2 | 27 | 886+886 |

■ ORDERING INFORMATION

Notes; 1) A means that relay is on the “reset” status when delivery; D means that relay is on the “set” status when delivery

2) If water cleaning is requested after relay is assembled on PCB, please contact us for suggestion about suitiable parts.

■ OVERALL AND MOUNTING DIMENSIONS

■ LATCHING RELAYS OPERATING GUIDE

1. Relay is on the "reset or set" status when being released from stock, with the consideration of shock, with the 
consideration of shock risen from transit and relay mounting, relay would be changed to "set" or "reset" status, 
therefore, when application (connecting the power supply), please reset the relay to "set" or "reset" status on request.

2. In order to maintain "set" or "reset" status, energized voltage to coil should reach the rated voltage, impulse width
should be 5 times more than "set" or "reset" time. Do not energize voltage to "set" coil and "reset" coil simultaneously. 
And also long energized time ( more than 1 min.) should be avoided.

3. The terminals of relay without twisted copper wire can not be tin-soldered, can not be moved willfully, more over two 
terminals can not be fixed at the same time.

Handouk Electronics Co., Ltd                                           EMAIL:sales@handouk.co.kr

# Text boxes

#### HL2-L