■ FEATURES

|  | ● Slim size (width 5mm) ● High breakdowm voltage 4kV (between coil and contacts) ● Surge voltage up to 6kV (between coil and contacts) ● Clearance/creepage distance: 8mm ● Meeting VDE0700,0631 reinforce insulation ● High sensitive: 170mW ● Sockets available ● 1 Form A and 1 Form C configurations ● Environmental friendly product (RoHs compliant) ● Outline Dimensions: (28.0X5.0X15.0)mm |
| --- | --- |

■ CONTACT  DATA

| Contact arrangement | 1A | 1C |
| --- | --- | --- |
| Contact resistance | 100mΩ(at 1A 6VDC) Gold plated:30mΩ(at 1A 6VDC) |
| Contact material | AgNi,AgSnO2 |
| Contact Ratings(Res. load) | 6A 250VAC / 30VDC |
| Max Switching Voltage | 400VAC / 125VDC |
| Max Switching Current | 6A |
| Max Switching Power | 1,500VA / 180W |
| Mechanical endurance | 1X107ops |
| Electrical endurance | 6X104ops (at 85℃) | (NO)3 X 104ops (at 85℃) (NC)1 X 104ops (at 85℃) |

■ CHARACTERISTICS

| Insulation Resistance | 100MΩ( at 500VDC) |
| --- | --- |
| Dielectric Strength | Between coil& Contacts | 4,000VAC 1min |
|  | Between open Contacts | 1,000VAC 1min |
| Operate Time(at nomi. volt) | 8ms max. |
| Release Time(at nomi. volt) | 4ms max. |
| Shock Resistance | Functional | 49m/s2 |
|  | Destructive | 980m/s2 |
| Vibration Resistance | 10 Hz to 55Hz 1mm DA |
| Humidity | 5% to 85% RH |
| Ambient temperature | -40℃ to 85℃ |
| Termination | PCB |
| Unit Weight | Approx .5.4g |
| Construction | Wash tight, Flux proofed |

Notes: 1) The data shown above are initial values.

2) Please find coil temperature curve in the characteristic curves below.

3) When install 1 Form C type of HS1, please do not make the relay side with 5mm width down.

■ COIL

| Coil power | 5 to 24VDC: 170mW 48VDC,60VDC: 210mW |
| --- | --- |

■ COIL DATA

| Nominal Voltage VDC | Pick-up Voltage VDC | Drop-out Voltage VDC | Max. Allowable Voltage | Coil Resistance Ω |
| --- | --- | --- | --- | --- |
| 5 | 3.75 | 0.25 | 7.5 | 147×(1±10%) |
| 6 | 4.50 | 0.30 | 9.0 | 212×(1±10%) |
| 9 | 6.75 | 0.45 | 13.5 | 476×(1±10%) |
| 12 | 9.00 | 0.60 | 18 | 848×(1±10%) |
| 18 | 13.5 | 0.90 | 27 | 1,906×(1±15%) |
| 24 | 18.0 | 1.20 | 36 | 3,390×(1±15%) |
| 48 | 36.0 | 2.40 | 72 | 10,600×(1±15%) |
| 60 | 45.0 | 3.00 | 90 | 16,600×(1±15%) |

Notes: When require pick-up voltage=70% nominal voltage,special order allowed.

■SAFETY APPROVAL RATINGS

| UL&CUL | Resistive: 6A 30VDC 6A 277VAC Pilot duty: R300 B300 |
| --- | --- |
| VDE | 6A 30VDC / 6A 250VAC |

Notes: Only some typical ratings are listed above. If more details are required, please contact us.

■ ORDERING INFORMATION

■ OUTLINE DIMENSIONS, WIRING DIAGRAM AND PCB LAYOUT          Unit:mm

Remark: 1) In case of no tolerance shown in outline dimension: outline dimension≤1mm,tolerance should be±0.2mm;outline

Dimension ＞1mm and ≤5mm,tolerance should be ±0.3mm；outline dimension >5mm ,tolerance should be± 0.4mm.

2) The tolerance without indicating for PCB layouts is always ±0.1mm.

■ CHARATERISTIC CURVES

Disclaimer

This datasheet  is for the customers’  reference. All the specifications are subject  to change without notice.

We could not evaluate all the performance and all the parameters for every possible application. 
Thus the user should be in a right position to choose the suitable product for their for their own application. 
If there is any query, please contact HANDOUK for the technical service. 
However, it is the user’s responsibility to determine which product should be used only.

# Text boxes

#### HS1