HANDOUK

■ FEATURES

● High switching capacity
1A : 10A 250VAC / 8A 30VDC 
2A, 1AB : 8A 250VAC / 30VDC

● High sensitivity : 200Mw

● 4kV dielectric strength (Between coil & contacts)

● Single side stable and Latching types available

● 1A, 2A, 1AB contact arrangement

( CONTACTS                                   ( SPECIFICATION

| Contact Form | 1A | 2A | 1AB |  | Insulation Resistance | 1000M( 500VDC |
| --- | --- | --- | --- | --- | --- | --- |
| Initial Contact Resistance | 30m( (at 24VDC 1A) |  |  |  |
|  |  |  | Dielectric Strength between | coil & contacts (1min) | 1A, 1A+1B: 4,000VAC |
| Contact Material | AgNi. AgNi + Au |  |  |  | 2A : 2,000VAC |
| Contact Rating (Resistance) | 10A, 250VAC 8A, 30VDC | 8A, 250VAC 8A, 30VDC |  |  | Open contacts | 1,000VAC, 1 min |
|  |  |  |  | Pulse width of coil | 20ms(Recom. 100ms to 200ms) |
| Max. Switching Power | 2500VA 240W | 2,000VA 240W |  | Operate Time | Max. 10ms |
|  |  |  |  | Release Time | Max. 10ms |
| Max. Switching Voltage | 277VAC |  | Max. operating frequency (Under rated load) | 20cycles / min. |
| Max. Switching Current | 10A | 8A |  | Temperature rise | 50K Max.(at nomi. Volt.) |
| Electrical Life | 1×105ops(2Form A:3×104ops) |  | Ambient Temperature | -40 ~ +70 (C |
| Mechanical Life | 5×107 ops |  | Vibration Resistance | 1.5 mm DA 10~55Hz |
|  |  | Shock Resistance | 100 m/s 2 |
|  |  |  |  | Terminals | PCB |
|  |  |  |  | Weight | Approx. 6g |
|  |  |  |  | Construction | Sealed IP67 & Flux proof |
|  |  |  |  | Size | 20.×15×10.2 |

( COIL  DATA

at 23℃

| Nominal Voltage VDC | Coil resistance Ω(±10%) | Pick-up (set/reset) Voltage VDC(max) | Drop-out Voltage VDC(min) | Coil Power |
| --- | --- | --- | --- | --- |
| 1A, 1A + 1B single side stable 1 coil latching | 3 | 45 | 2.1 | 0.3 | 200mW |
|  | 5 | 125 | 3.5 | 0.5 |  |
|  | 6 | 180 | 4.2 | 0.6 |  |
|  | 9 | 405 | 6.3 | 0.9 |  |
|  | 12 | 720 | 8.4 | 1.2 |  |
|  | 24 | 2880 | 16.8 | 2.4 |  |

at 23℃

| Nominal Voltage VDC | Coil resistance Ω(±10%) | Pick-up (set/reset) Voltage VDC(max) | Drop-out Voltage VDC(min) | Coil Power |
| --- | --- | --- | --- | --- |
| 2 Form A single side stable | 3 | 32.1 | 2.1 | 0.3 | 280mW |
|  | 5 | 89.3 | 3.5 | 0.5 |  |
|  | 6 | 129 | 4.2 | 0.6 |  |
|  | 9 | 289 | 6.3 | 0.9 |  |
|  | 12 | 514 | 8.4 | 1.2 |  |
|  | 24 | 2056 | 16.8 | 2.4 |  |
| 2 coil latching | 3 | 32.1+32.1 | 2.1 | - | 280mW |
|  | 5 | 89.3+89.3 | 3.5 | - |  |
|  | 6 | 129+129 | 4.2 | - |  |
|  | 9 | 289+289 | 6.3 | - |  |
|  | 12 | 514+514 | 8.4 | - |  |
|  | 24 | 2056+2056 | 16.8 | - |  |

( ORDER DESIGNATION

( OUTLINE DIMENSIONS, PC BOARD LAYOUT AND WIRING DIAGRAM

Notice
1. Relay is on the "reset" status when being released from stock, with the condition of shock risen from transit 
    and relay mounting, relay would be changed to "set" status, therefore, when application (connecting the power supply),
    please reset the relay to "set" or "reset"status on request.
2. In order to maintain "set" or "reset" status, energized voltage to coil should reach the rated voltage, impulse width 
    should be 5 times more than "set" or "reset" time. Do not energize voltage to "set" coil and "reset" coil simultaneously. 
    And also long energized time (more than one min.) should be avoid.
3. In order to avoid changing operate voltage, products should not be kept in strong magnetic field during transportation,
    storage and application.

# Text boxes

#### HT1