HANDOUK

■ FEATURES

● 1Form A, 2Form A, 1 Form A 1 Form B contact

● High sensitivity

● Latching types available

● High switching capacity:1A:8A/250VAC, 
2A:5A/250VAC

( CONTACTS                                   ( SPECIFICATION

| Contact Form | 1A | 2A | 1AB |  | Insulation Resistance | 1000M( 500VDC |
| --- | --- | --- | --- | --- | --- | --- |
| Initial Contact Resistance | 50m( (at 6VDC 1A) |  |  |  |
|  |  |  | Dielectric Strength | Contact to coil | 3000Vrms, 1 min |
| Contact Material | AgNi |  |  | Contact to contact | 1000Vrms, 1 min |
| Contact Rating (Resistance) | 8A, 250VAC 5A, 30VDC | 5A, 250VAC 5A, 30VDC |  |  | Contact sets | 2000Vrms, 1 min |
|  |  |  |  | Operate Time | Max. 10ms |
| Max. Switching Power | 2000VA 150W | 1,250VA 150W |  | Release Time | Max. 5ms |
|  |  |  |  | Set Time ( latching) | Max. 10ms |
| Max. Switching Voltage | 380VAC, 125VD C |  | Re-Set Time ( latching) | Max. 10ms |
| Max. Switching Current | 8A | 5A |  | Ambient Temperature | -40 ~ +70 (C |
| Electrical Life | 1×105ops |  | Vibration Resistance | 2 mm 10~55Hz |
| Mechanical Life | 1×107 ops |  | Shock Resistance | 196 m/s 2 (20g) functional |
| ( COIL |  |  |  |
| Coil Nominal Power | single side stable | 300mW |  |  | 980 m/s2 (100g) destructive |
|  | 1 coil bistable | 150mW |  | Terminals | PCB |
|  | 2 coil bistable | 300mW |  | Construction | Sealed IP67 & Flux proof |
| Coil Voltage | See table |  | Weight | 20.2×11×10.4 |

( COIL  DATA

Single side stable    (300mW)     20℃

| Order Number | Nominal Voltage VDC | Pick-up Voltage VDC(max) | Drop-out Voltage VDC(min) | Coil resistance Ω(±10%) | Max. allow Voltage at 70℃ VDC |
| --- | --- | --- | --- | --- | --- |
| 3-□ | 3 | 2.4 | 0.3 | 30 | 3.9 |
| 5-□ | 5 | 4.0 | 0.5 | 83 | 6.5 |
| 6-□ | 6 | 4.8 | 0.6 | 120 | 7.8 |
| 9-□ | 9 | 7.2 | 0.9 | 270 | 11.7 |
| 12-□ | 12 | 9.6 | 1.2 | 480 | 15.6 |
| 24-□ | 24 | 19.2 | 2.4 | 1920 | 31.2 |

Latching（1 coil）  (150mW)   20℃             Latching（2 coil）  (300mW)    20℃

| Order Number | Nominal Voltage VDC | Set-Reset Voltage VDC (max) | Coil Resistance Ω （±10%） | Max. allow Voltage at 70℃ VDC |  | Order Number | Nominal Voltage VDC | Set、Reset Voltage VDC (max) | Coil Resistance Ω （±10%） | Max. allow Voltage at 70℃ VDC |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 3-□-L1 | 3 | 2.4 | 60 | 3.9 |  | 3-□-L2 | 3 | 2.4 | 30 | 3.9 |
| 5-□-L1 | 5 | 4.0 | 167 | 6.5 |  | 5-□-L2 | 5 | 4.0 | 83 | 6.5 |
| 6-□-L1 | 6 | 4.8 | 240 | 7.8 |  | 6-□-L2 | 6 | 4.8 | 120 | 7.8 |
| 9-□-L1 | 9 | 7.2 | 540 | 11.7 |  | 9-□-L2 | 9 | 7.2 | 270 | 11.7 |
| 12-□-L1 | 12 | 9.6 | 960 | 15.6 |  | 12-□-L2 | 12 | 9.6 | 480 | 15.6 |
| 24-□-L1 | 24 | 19.2 | 3840 | 31.2 |  | 24-□-L2 | 24 | 19.2 | 1920 | 31.2 |

( ORDER DESIGNATION

( OUTLINE DIMENSIONS, PC BOARD LAYOUT AND WIRING DIAGRAM

# Text boxes

#### HT2