HANDOUK

■ FEATURES

| * 100A switching capability. * Strong resistance ability to shock & vibration * Heavy load up to 27.7kVA * 4kV dielectric strength between coil and contacts. * Micro switch on mounting board available. |  |
| --- | --- |

■ CONTACT  DATA

| Contact Arrangement | 1 Form A (SPST) |
| --- | --- |
| Voltage drop2) | Typ.: 50mV (at 10A) Max.:250mV (at 10A) |
| Contact material | AgSnO2, AgCdO |
| Contact Ratings(Res. Load) | 100A 277VAC/28VDC |
| Max Switching Voltage | 440VAC / 45VDC |
| Max Switching Current | 100A |
| Max Switching Power | 27,700VA / 2,800W |
| Life Expectancy | Electrical：2 x 104 ops |
|  | Machanical：1 x 105 ops |

■ CHARACTERISTICS

| Insulation Resistance | 100MΩ |
| --- | --- |
| Dielectric Strength between | coil & contacts | 4,000VAC 1 min. |
|  | open contacts | 2,000VAC 1 min. |
| Creepage distance | 8 mm |
| Operate Time | 20 ms max. |
| Release time | 20 ms max. |
| Shock Resistance | Functional | 100m/s2 |
|  | Destructive | 1,000m/s2 |
| Vibration Resistance | 10Hz to 55Hz 1.0mm DA |
| Humidity | 98% RH, 40°C |
| Ambient temperature | -40°C ~ 70°C |
| Termination | PCB & QC |
| Unit weight | Approx 100g |
| Construction | Dust protected |

■COIL DATA

| Nominal Voltage (VDC) | Coil resistance ±10% Ω | Pick-up voltage VDC | Pilse Duration ms | Coil Power |
| --- | --- | --- | --- | --- |
| Standard | 6 | Single coil | 16 | ≤4.8 | 200 | 2.4W |
|  | 12 |  | 60 | ≤9.6 | 200 |  |
|  | 24 |  | 250 | ≤19.2 | 200 |  |
|  | 48 |  | 1000 | ≤38.4 | 200 |  |
|  | 6 | Double coil | 8+8 | ≤4.8 | 200 | 4.8W |
|  | 12 |  | 30+30 | ≤9.6 | 200 |  |
|  | 24 |  | 125+125 | ≤19.2 | 200 |  |
|  | 48 |  | 500+500 | ≤38.4 | 200 |  |

Notes: 1) The data shown above are initial values.
        2) Equivalent to the max. Initial contact resistance is 50mΩ (at 1A 24VDC), and measured 
          when coil is energized with 100% nominal voltage at 25°C.
        3) When requiring other nominal voltage, special order allowed.
     4) Max. allowable coil voltage is recommended  in 130%.
Notice 
1. Relay is on the "set" status when being released from stock, with the consideration of shock risen
    from transit and relay mounting, relay would be changed to "reset" status, therefore, 
    when application (connecting the power supply), please reset the relay to "set" or "reset" status
    on request.
2. In order to maintain "set" or "reset" status, energized voltage to coil should reach the rated
    voltage, impulse width should be 5 times more than "set" or "reset" time. Do not energize voltage
    to "set" coil and "reset" coil simultaneously. And also long energized time (more than 1 min)
    should be avoided.
3. The terminals of relay without twisted copper wire can not be tin-soldered, can not be moved
    willfully, more over two terminals can not be fixed at the same time.

■ORDERING CODE

Notes: 1) When ordering sensitive type, please specify the exact coil power.
        2) HT4 is an environmental friendly product.

■OUTLINE DIMENSIONS, WIRING DIAGRAM & PC BOARD LAYOUT (Unit : mm)

Remark : In case of no taloerance shown in outline dimension : Outline dimension≤ 1mm, tolerance

should be ±0.2mm; Outline dimension 〉 1mm and ≤ 5mm, tolerance should be ±0.3mm; outline dimension 〉5mm, tolerance should be ±0.4mm.

# Text boxes

HT4