HANDOUK

■ FEATURES

| ● High contact Load ●The relays are designed and manufactured in accordance with the Standards of DIN IEC 61810. part 1-00/VED 0435,part 201,which are also in accordance with the Low Voltage directive(LVD). ●The advantage of the polarized latching relays is the Pulse driven operation of 30 milliseconds. Therefore there is a low need of setting power and the coil heating can be neglected. Relay can be set by manual operation. ●Dimension: 76X81X22mm |  |
| --- | --- |

■ CONTACT  DATA

| Contact Form | 2 Form A |
| --- | --- |
| Contact Material | Silver Alloy |
| Load | Resistive load(Cos Φ1) |
| Contact Ratings | 100A |
| Max Switching Voltage | 440VAC |
| Max Switching Power | 25,000VA |
| Contact Resistance | 2mΩMax at 6VDC 1A |
| Life Expectancy | Electrical | 20,000 Operations(6cpm with 90A) |
|  | Mechanical | 500,000 Operations(at180Operations/minute) |

■ CHARACTERISTICS

| Insulation Resistance | 100MΩMin (at 500VDC) |
| --- | --- |
| Dielectric Strength Between open Contacts | 1,000VAC (for one minute) |
| Between Contacts and coil | 4,000VAC (for one minute) |
| Operate Time | 30ms |
| Action Time | <15ms |
| Temperature Range | -25℃ to+75℃ |
| Shock Resistance | Operating Extremes：10G |
|  | Damage Limits：100G |
| Vibration Resistance | 10 Hz~ 55Hz, 1.5mm |
| Humidity | 40-95% |
| Weight | Approx .240g |

■COIL DATA

| Nominal Voltage (VDC) | Rated Current (mA) | Operate Coil (Ω ±10%) | Release Voltage (VDC) | Operating Voltage (VDC) | Rectangular Pulse Width(ms) |
| --- | --- | --- | --- | --- | --- |
| 6 | 1330 | 4.5 | 80%(min) | 80%(min) | Min.80 |
| 12 | 667 | 18 |  |  |  |
| 16 | 500 | 32 |  |  |  |
| 24 | 333 | 72 |  |  |  |
| Double coil 8.0W |  |  |  |

■ OUTLINE DIMENSIONS AND WIRING DIAGRAM                                  Unit:mm

Remark: In case of no tolerance shown in outline dimension: outline dimension≤1mm,tolerance should be±0.2mm; outline

dimension〉1mm and ≤5mm,tolerance should be ±0.3mm；outline dimension >5mm ,tolerance should be± 0.4mm.

Disclaimer

This datasheet is for the customers’ reference. All the specifications are subject to change without notice.

# Text boxes

HT5