HANDOUK

■ FEATURES

● Small size, 100A switching capability.

● Low coil consumption, ultra-low temperature rise.

● Low contact resistance.

● Strong anti-shock and anti-viboration capability.
● Dimensions: (40.0ⅹ30.0ⅹ22.0)mm
● Customized terminals like shunt, braided Cu-wire etc.

| CONTACT DATA |  | CHARACTERISTICS |
| --- | --- | --- |
| Contact form | 1A/1B |  | Operate Time | 30ms Max |
| Contact Resistance | Max.1.2mΩ(at 1A 6VDC) |  | Release Time | 30ms Max |
| Contact material | SgSnO2 |  | Relative Humidity | 45%-90%RH |
| Contact rating(Res. Load) | 100A 250VAC |  | Dielectric strength | Coil& contacts | 4,000VAC 50/60Hz(1 Min) |
| Max. switching Voltage | 250VAC |  |  | Between Open contacts | 1,800VAC 50/60Hz(1 Min) |
| Max. switching current | 100A |  | Insulation resistance | 1,000MΩ Min.(500VDC) |
| Max. switching power | 25KVA |  | Ambient temperature | -40℃ to 70℃ |
| Life | Mechanical life | 5ⅹ105ops |  | Impulsion | 98m/s2 |
|  | Electrical life | 6ⅹ103ops |  | Vibration | 10-55HZ,1.5mm |
| Max. Short-circuit current | 3000A/10ms |  | Weight(without accessories) | 60g |

COIL DATA                                                                       AT 20℃

| Rated coil ( VDC ) | Coil resistance(Ω)±10% | Coil power (W) | Operate Voltage (VDC) | Release Voltage (VDC) | Over Voltage (VDC) | Impulse Duration (ms) |
| --- | --- | --- | --- | --- | --- | --- |
|  | Single coil | Double coil | Single coil | Double coil |  |  |  |  |
| 9 | 67.5 | 34/34 | 1.2W | 2.4W | ≤75% | ≤75% | ≤150% | ≥100ms |
| 12 | 120 | 60/60 |  |  |  |  |  |  |
| 24 | 480 | 240/240 |  |  |  |  |  |  |
| 48 | 1,920 | 960/960 |  |  |  |  |  |  |

( ORDER INFORMATION

Dimension、wiring diagram (Unit: mm)

Note: No tolerance marked. When dimension is ≤1mm, the tolerance shall be±2; when dimension is 1-5mm,

The tolerance shall be±0.3; when dimension is >5mm, the tolerance shall be±0.5.

Schematic diagram of a typical specification (Unit: mm)

Typical application

- Smart meter

- Electric remote control

- Power composite switch

- Leakage protection

Notice

- The factory default of the contacts is to stay closure (reset), It’s possible that the status will be changed with be changed with impact during

shipment or installation. Please make sure the status of the contacts stay reset before using.

- To guarantee the latching relay operates reliably, the excitation voltage to coil should meet the rated value and

Impulse duration needs to exceed 3 times of the operation time. For double coil type latching relay, please neither apply

voltage signal to both coils at the same time nor apply with long time (over 1 min).

- Latching relays without copper braided wires, the loaded PIN can neither be tin soldered nor be wrenched. Rigid

fixing of the two pins is also not allowed.

- Magnetic latching relay is polarized relay. If customer needs different kinds of polarity from the data sheet, please inform us.

- Please handle the latching relays with care during factory’s incoming-inspection and when put in use, do not let the relay

drops which will impact the parameter. Please make strict distinction between relay made for.

# Text boxes

#### HT91-100A