HANDOUK

►FEATURES

| ● 2,500V dielectric strength ● Photo isolation ● Built-in snubber ● Zero cross or random turn-on |  |  |
| --- | --- | --- |

►CHARACTERISTICS

| MODEL | DC : AC | AC : AC |
| --- | --- | --- |
| Controlling Voltage | 3-14VDC,3-32VDC | 3-14VDC,3-32VDC |
| Controlling current | 5-25mA | 5-25mA |
| Make-on Voltage | 3VDC | 3VDC |
| Break-off Voltage | 1VDC | 1VDC |
| Reverse Voltage | 32VDC | 32VDC |
| Load Voltage | 40-440VAC | 40-440VAC |
| Load Current | 60A ~ 150A | 200A ~ 350A |
| Instant Voltage | 1,200VAC | 1,200VAC |
| Voltage Drop in On | Min. 1.6VAC | Min. 1.6VAC |
| On-off Time | Max. 10mS | Max. 10mS |
| Leakage Current in off | Max. 10mA | Max. 10mA |
| Dielectric Strength | Min. 2,500VAC | Min. 2,500VAC |
| Insulation Resistance | 500M ohm (at 500VDC) | 500M ohm (at 500VDC) |
| Ambient Temperature | -30~80°C | -30~80°C |
| Weight | 135g | 235g |
| Indicate Methods | LED | LED |
| Dimension(LxWxH) | 94 x 25 x 36.2mm | 94 x 34 x 43mm |

►ORDERING INFORMATION

►OUTLINE dimensions,WIRING DIAGRAM AND MOUNTING HOLES    
                                                                   ( Unit  : mm )

# Text boxes

#### SK