►FEATURES

- Offers excellent board space savings

- Surge withstand voltage up to 2500V,meets FCC Part 68

and Telecordia

- Meets EN60950/EN41003

- SMT and DIP types available

- High contact capacity 2A 30VDC

- Low power consumption

- Single side stable and latching type available

- Environmental friendly product (RoHS compliant)

- Outline Dimensions: (10. 0 x6.5 x5.4) mm

►CONTACT DATA

| Contact arrangement | 2C |
| --- | --- |
| Contact resistance | 70mΩ |
| Contact Material | Silver alloy, Gold clad |
| Contact Rating (resistive) | 2A/30VDC; 0.5A/125VAC |
| Max. Switching Current | 2A |
| Max. Switching voltage | 220VDC/250VAC |
| Max. Switching Power | 60W/62.5 VA |
| Min. applicable load | 10mV 10µA |
| Mechanical endurance | 1 x108ops |
| Electrical endurance | 1 x 105 ops (at 2A 30VDC) |
|  | 1 x105 ops (at 0.5A 125VAC) |

►COIL data

Single side stable

| Order Number | Nominal Voltage VDC | Pickup voltage (VDC) | Drop-up voltage (VDC) | Coil Resistance Ω | Nominal Power mW | Max. Allowable Voltage VDC |
| --- | --- | --- | --- | --- | --- | --- |
| BC1-1.5 | 1.5 | 1.13 | 0.15 | 16x(1±10%) | 140 | 2.2 |
| BC1-3 | 3 | 2.25 | 0.3 | 64.3x(1±10%) | 140 | 4.5 |
| BC1-4.5 | 4.5 | 3.38 | 0.45 | 145x(1±10%) | 140 | 6.7 |
| BC1-5 | 5 | 3.75 | 0.5 | 178x(1±10%) | 140 | 7.5 |
| BC1-6 | 6 | 4.5 | 0.6 | 257x(1±10%) | 140 | 9.0 |
| BC1-9 | 9 | 6.75 | 0.9 | 579x(1±10%) | 140 | 13.5 |
| BC1-12 | 12 | 9 | 1.2 | 1028x(1±10%) | 140 | 18.0 |
| BC1-24 | 24 | 18 | 2.4 | 2880x(1±10%) | 200 | 36.0 |

1  coil latching

| Order Number | Nominal Voltage VDC | Pickup voltage (VDC) | Drop-up voltage (VDC) | Coil Resistance Ω | Nominal Power mW | Max. Allowable Voltage VDC |
| --- | --- | --- | --- | --- | --- | --- |
| BC1-1.5-L1 | 1.5 | 1.13 | 1.13 | 22.5x(1±10%) | 100 | 3.0 |
| BC1-3-L1 | 3 | 2.25 | 2.25 | 90x(1±10%) | 100 | 6.0 |
| BC1-4.5-L1 | 4.5 | 3.38 | 3.38 | 203x(1±10%) | 100 | 9.0 |
| BC1-5-L1 | 5 | 3.75 | 3.75 | 250x(1±10%) | 100 | 10.0 |
| BC1-6-L1 | 6 | 4.5 | 4.5 | 360x(1±10%) | 100 | 12.0 |
| BC1-9-L1 | 9 | 6.75 | 6.75 | 810x(1±10%) | 100 | 18.0 |
| BC1-12-L1 | 12 | 9 | 9 | 1440x(1±10%) | 100 | 24.0 |
| BC1-24-L1 | 24 | 18 | 18 | 2880x(1±10%) | 200 | 36.0 |

►characteristics

| Insulation resistance | 1000MΩ (at 500VDC) |
| --- | --- |
| Dielectric strength | Between coil & contacts | 1800VAC 1min |
|  | Between open contacts | 1000VAC 1min |
|  | Between contact sets | 1800VAC 1min |
| Surge withstand voltage Between open contacts (10 x160µs) Between coil & contacts (2 x10µs) | 1500VAC (FCC part 68) 2500VAC(Telecordia) |
| Operate time (Set time) | 3ms max. |
| Release time (Reset time) | 3ms max |
| Ambient temperature | -40℃ to 85℃ |
| Humidity | 98% RH, 40℃ |
| Vibration resistance | Functional | 10Hz to 55Hz 3.3mm DA |
|  | Destructive | 10HZ to 55HZ 5.0mm DA |
| Shock resistance | Functional | 735m/s2 |
|  | Destructive | 980 m/s2 |
| Termination | DIP.SMT |
| Unit weight | Approx.0.8g |
| Construction | Wash tight |
| Coil power | Single side stable | 140mW |
|  | 1 coil latching | 100mW |
| Temperature rise | 50K max. |

notes: The data shown above are initial values.

►ORDERING INFORMATION

►OUTLINE DIMENSIONS, WIRING DIAGRAM AND PC BOARD LAYOUT                               Unit:mm

Remark 1).In case of no tolerance shown in outline dimension; outline dimension≤1mm,tolerance should be ±0.2mm;outline dimension>1mm and≤5mm,tolerance should be ±0.3mm; outline dimension >5mm, tolerance should be ±0.4mm.

2).The tolerance without indicating for PCB layout is always ±0.1mm.

# Text boxes

#### BC1