►FEATURES

● DIL Pitch Terminals .High Sensitivity.

● Dielectric 1000VAC.

● Fully sealed (immer1sion clearable).

● High Reliability bifurcated Contact.

● Application for

Telecommunication Equipment.

Office Equipment, Security Alarm Systems.

Measuring instruments.

Medical Monitoring Equipment. etc.

►CONTACT DATA

| Contact Arrangement | 2C（Bifurcated Crossbar） |
| --- | --- |
| Contact Material | Silver alloy |
| Contact Rating (resistive) | 1A 120VAC, 2A 24VDC |
| Min. Switching load | 1mA/5Vdc（Reference Value） |
| Max. Switching Current | 2A |
| Max. Switching Power | 60W 120VA |
| Max. Switching Voltage | 60VDC 240VAC |
| Contact Resistance or Voltage drop | (100mΩ |
| Operation life | Electrical | 1 x 105 at 30 Operations per minute |
|  | Mechanical | 1 x 107 at 60 Operations per minute |

CAUTION: Relays previously tested or used above 10mA resistive at 6VDC maximum or peak AC open circuit are not recommended for subsequent use in law level applications.

►COIL PARAMETER

| Coil voltage (VDC) | Coil resistance (Ω(10%) | Pickup voltage(max) (VDC) | release voltage(min) (VDC) | Applicable Voltage (Max) (VDC) |
| --- | --- | --- | --- | --- |
|  | 0.15W | 0.2W | 0.36W | 0.45W | 0.15W | 0.2,0.36,0.45W | 0.15W | 0.2,0.36,0.45W |  |
| 3 | 60 | 45 | 25 | 20 | 2.4 | 2.25 | 0.15 | 0.3 | 3.9 |
| 5 | 167 | 125 | 70 | 56 | 4 | 3.75 | 0.25 | 0.5 | 6.5 |
| 6 | 240 | 180 | 100 | 80 | 4.8 | 4.5 | 0.3 | 0.6 | 7.8 |
| 9 | 540 | 405 | 220 | 180 | 7.2 | 6.75 | 0.45 | 0.9 | 11.7 |
| 12 | 960 | 720 | 400 | 320 | 9.6 | 9 | 0.6 | 1.2 | 15.6 |
| 24 | 3,840 | 2,800 | 1,600 | 1,280 | 19.2 | 18 | 1.2 | 2.4 | 31.2 |
| 48 |  |  | 6,400±15% | 5,100±15% |  | 36 |  | 4.8 | 62.4 |

CAUTION: 1.The use of any coil voltage less than the rated coil voltage will compromise the operation of the relay.

2.Pickup and release voltage are for test purposes only and are not to be used as design criteria.

►OPERATION CONDITION

| Insulation Resistance | 100MΩ Min at 500VDC |
| --- | --- |
| Dielectric Strength | Open Contacts | 500 for one minute, 750 VAC for one second |
|  | Contact and Coil | 1,000 for one minute , 1,250 VAC for one second |
| Operate Time | 6ms |
| Release Time | 4ms |
| Temperature Range | -30℃ to + 85 ℃ |
| Shock Resistance | Operating Extremes | 10G |
|  | Damage Limits | 50G |
| Vibration resistance | 10~55Hz Double amplitude 1.5mm |
| Humidity | 40 ~ 85% |
| Weight | Approx. 5g |

►ORDERING INFORMATION

►DIMENSIONS  (Unit: mm)

Dimensions                                        Wiring diagram (Bottom view)

NOTES 1).Dimensions are in millimeter.

2).Inch equivalents are given for general information only.

# Text boxes

#### BC3