HANDOUK

►FEATURES

● Semi-multi power supply voltage ● Exclusive C-MOS IC permits miniaturization and assures high performance ● High repeat accuracy : ±5% including the initial value ● Short resetting time : 0.1 second max. including the time when the timer resets in operation ● Large transparent time setting knob facilitates time setting ● Equipped with a LED power-ON indicator ● Environmental friendly product (RoHs compliant) ● Outline Dimensions: 28.0 x 21.5 x 52.0mm

►CHARACTERISTICS

| Accuracy of operating time(Max) | ±5% |
| --- | --- |
| Setting error (Max.)1) | ±10%±50ms |
| Reset time (Max.) | 0.1ms(Including halfway reset |
| Reset voltage (Max.) | 10% of rated supply voltage |
| Influence of Voltage (Max.)1) | ±2% |
| Influence of temperature (Max.)1) | ±2% |
| Insulation resistance (Min.) | 100M ohm (at 500VDC) |
| Dielectric Strength Between | contacts | 1,500VAC 1min |
|  | circuits | 1,500VAC 1min |
|  | contact sets | 1,000VAC 1min |
| Vibration resistance | Destruction | 10 to 55Hz, 0.75mm single amplitude |
|  | Malfunction | 10 to 55Hz, 0.50mm single amplitude |
| Shock resistance | Destruction | 1,000 m/s2 (100g) |
|  | Malfunction | 100 m/s2 (10g) |
| Ambient temperature | Operating | -10°C to 50°C (with no icing) |
|  | Storage | -25°C to 65°C (with no icing) |
| Ambient humidity | 35% to 85% RH |
| Malchanical life (Min) | 1x107 ops (under no load at 1,800 ops/h) |
| Electrical life (Min.) | ST-2 : 1x105 ops (7A 250VAC/30VDC. Res. load) ST-4 : 1x105 ops (5A 250VAC/30VDC. Res. load) |
| Enclosure rating | IP40 |
| Weight | 50g |

Notes: 1) Add ±10ms to above value for the 1s range model

►TIME RANGE

| Code | Rated time | Time setting range | Code | Rated time | Time setting range |
| --- | --- | --- | --- | --- | --- |
| A | 1 second | 0.05 to 1s (Scale:0.05) | F | 3 min | 0.1 to 3min(Scale:0.1) |
| B | 6 seconds | 0.37 to 6s (Scale:0.2) | G | 6 min | 0.2 to 6min(Scale:0.2) |
| C | 12seconds | 0.5 to 12s (Scale:0.4) | H | 12 min | 0.4 to 12min(Scale:0.4) |
| D | 30seconds | 1.5 to 30s (Scale:1) | I | 30 min | 1 to 30min(Scale:1) |
| E | 60seconds | 2.3 to 60s (Scale:2) | J | 60 min | 2 to 60min(Scale:2) |

►ORDERING INFORMATION

|  | ST-2 | A | 24VDC | XXX |
| --- | --- | --- | --- | --- |
| Type | ST-2 : 7A 250VAC/30VDC, 2pole ST-4 : 5A 250VAC/30VDC, 4pole |  |  |  |
| Timing range | A to L (Show in the timing range table) |  |  |  |
| Control voltages | 12, 24, 48VDC, 110, 220, 240VAC |  |  |  |
| Customer special code | Only for special requirements |  |  |  |

►OUTLINE DEMENSIONS

# Text boxes

#### ST