HANDOUK

►FEATURES

High switching 30A ( 1A )

SPDT & SPST configurations

PCB mounting, Plug-In type

Size (L x W x H)

32.4 x 27.8 x 28mm

►CONTACT DATA

| Contact Form | 1A , 1C |
| --- | --- |
| Contact Ratings | Standard | High Capacity |
|  | NO : 30A 240VAC 30A 28VDC NC : 20A 240VAC 20A 28VDC | NO : 40A 240VAC 40A 28VDC NC : 30A 240VAC 30A 28VDC |
| Contact Material | Ag Alloy |
| Max. Switching Voltage | 30A | 40A |
| Max. Switching Current | 30A | 40A |
| Max. Switching Power | 30A |
| Contact Resistance | 100mΩMax., at 6VDC 1A |
| Life Expectancy | Electrical | 100,000 Operations (at 30 ops a minute) |
|  | Mechanical | 10,000,000 Operations |

►OPERATION CONDITION

| Insulation Resistance | 100MΩ min (at 500VDC) |
| --- | --- |
| Dielectric Strangth | Between open Contacts | 1,500VAC (For one minute) |
|  | Between coil & Contacts | 2,500VAC (For one minute) |
| Operate time | 15ms |
| Release Time | 10ms |
| Shock resistance | Operating Extremes | 10G |
|  | Damage Limits | 100G |
| Vibration resistance | 10~55Hz Double amplitude |
| Humidity | 40~85% |
| Temperature Range | -40 ~ 70℃(-40~158°F) |
| Weight | Approx 36g |
| Safety Standard | UL | E197546 |
|  | TUV | R50056430 |

►COIL PARAMETER

| Nominal Voltage (VDC) | Coil Resistance at 20 C (Ω) 0.93W | Max Operate Voltage | Min. Release Voltage | Max. Applicable Voltage |
| --- | --- | --- | --- | --- |
| 3 | 9.7 | 2.25 | 0.3 | 3.9 |
| 5 | 26.9 | 3.75 | 0.5 | 6.5 |
| 6 | 38.8 | 4.5 | 0.6 | 7.8 |
| 9 | 87.1 | 6.75 | 0.9 | 11.7 |
| 12 | 154.9 | 9 | 1.2 | 15.6 |
| 24 | 619.4 | 18 | 2.4 | 31.2 |
| 48 | 2477.5 | 36 | 4.8 | 62.4 |

►ORDERING INFORMATION

※.High Capacity type has "T" Marking on under right side.

►DIMENSIONS  (Unit: MM)

S : Tap terminal enclosed

O : Tap terminal excluded

B : Bracketed

BO : Bracketed & Tap terminal excluded

►useful curve

# Text boxes

#### RB