■ FEATURES

- 30A 13.5VDC switching rating.

- 40A inrush at 13.5VDC

- Small size, lightweight 4g (8g: Twin Relay)

- Withstands high temperature, operating

under 105℃ ambient temperature.

- Heavy contact load switching current up to 30A.

- Size：12x12.9x9.9 ( Single relay ), 23.8x12.9x9.9 ( Twin relay )

■ Contact Data

| Contact Arrangement | 1A(SPST), 1C(SPDT) | 2A(DPST), 2C(DPDT) |
| --- | --- | --- |
| Contact Material | See below Chart | AgNi AgSnO2 |
| Contact Rating (resistive) |  | 1C: NO:30A,20A/14VDC; NC:25A,15A/14VDC |
| Max. Switching Power | 420W | 280W |
| Max. Switching Voltage | 24VDC Max. Switching Current:30A |
| Max. carrying current | NO: 40A for 2 minutes,30A for 1 hour(12VDC at 20℃); 35A for 2 minutes,25A for 1 hour (12VDC at 85℃) |
| Contact Resistance or Voltage drop | ≤30mV (at 10A) | Item 4.12 of IEC 61810-7 |
| Operation life | Electrical | 105 | Item 4.30 of IEC 61810-7 |
|  | Mechanical | 107 | Item 4.31 of IEC 61810-7 |

RE2-1C Contact tested data

| Contact Rating | Load Type | Contact Load current(A) | Frequency ops/min | Duty Cycle | Life Expectancy |
| --- | --- | --- | --- | --- | --- |
|  |  | NO | NC |  |  |  |
|  | Resistive Load | 20 | --- | 15 | 0.5 | 3 x 105 |
|  | Wiper reserve L=1.0mH | Make | 25 | 25 | 15 | 0.5 | 3 x 105 |
|  |  | Break | 5 | 5 |  |  |  |
|  | Motor reserve blocked L=0.77mH | 20A Inrush | 15 | 0.5 | 1 x 105 |
|  | Flasher Load | 3 x 21W | --- | 80 | 0.5 | 2 x 106 |
|  | Lamp | Inrush | 100 | --- | 6 | 1/6 | 1 x 105 |
|  |  | Steady state | 10 | --- |  |  |  |

■ OPERATION CONDITION

| Insulation Resistance | 1,000M Ω Min. at 500VDC | Item 7 of IEC 61810-5 |
| --- | --- | --- |
| Dielectric Strength Between | Contacts | 50Hz 500V | Item 6 of IEC 61810-5 |
|  | Contact and coil | 50Hz 500V | Item 6 of IEC 61810-5 |
| Shock Resistance | 300m/s2 6ms | IEC68-2-27 Test Ea |
| Vibration Resistance | 10~500Hz double amplitude 1.27mm 60m/s2 | IEC68-2-6 Test Fc |
| Terminals Strength | 10N | IEC68-2-21 Test Ua 1 |
| Solderability | 235℃±2℃ 3±0.5s | IEC68-2-20 Test Ta method 1 |
| Ambient Temperature | -40~105℃ |
| Relative Humidity | 85% (at 20℃) | IEC68-2-3 Test Ca |
| Mass | 4g (Q-type 9.5g) | Approx 8g |

■ ORDERING INFORMATION

■ COIL DATA

RE2-1C

| Norminal Coil Voltage VDC | Max. operating voltage | Min release voltage VDC | Rated current mA | Coil Resistance Ω±10% | Coil power Consumption W |
| --- | --- | --- | --- | --- | --- |
| 6 | 3.45 | 0.6 | 95 | 63 | 0.57 |
| 12 | 6.9 | 1.2 | 47.5 | 254 |  |
| 24 | 13.8 | 2.4 | 23.7 | 1,010 |  |
| 6 | 3.45 | 0.6 | 133.3 | 45 | 0.80 |
| 12 | 6.9 | 1.2 | 66.7 | 180 |  |
| 24 | 13.8 | 2.4 | 33.3 | 720 |  |
| * Max Applicable Voltage : 23℃ 170%, 70℃ 130% |

RE2-2C

| Nominal Coil Voltage | Coil Voltage VDC | Coil Resistance Ω±10% | Pickup Voltage VDC(MAX) （58% of rated Voltage) | Release voltage VDC(min) (12.5% of rated Voltage) | Coil power Consumption W | Operate Time ms | Release Time ms |
| --- | --- | --- | --- | --- | --- | --- | --- |
|  | Rated | MAX |  |  |  |  |  |  |
| 10 | 10 | 12 | 181 | 5.7 | 1.25 | 0.55 | ≤4 | ≤1.5 |
| 12 | 12 | 14.4 | 254 | 6.9 | 1.5 | 0.57 |  |  |
| 24 | 24 | 28.8 | 1,010 | 13.8 | 3 | 0.57 |  |  |

CAUTION: 1). The use of any coil voltage less than the rated coil voltage will compromise the operation of the relay.

2). Pick-up and release voltage are for test purposes only and are not to be used as design criteria.

■ Sound Pre. Characteristics(Q type):

Operation noise:<50db

Coil voltage:12VDC

■ OVERALL AND MOUNTING DIMENSIONS

NOTES: 1). Dimensions are in millimeters.

2). Inch equivalents are given for general information only.

# Text boxes

#### RE2