■ FEATURES

- Twin structure of RF2 type.

- Small size, light weight.

- Low coil power consumption.

- PC board mounting.

- Suitable for household appliances, electrical equipment

automation system, and automobile industry application.

- Size：29.6 x 18 x 20mm

■ Contact Data

| Contact Arrangement | 2A(DPST), 2C(DPDT) | 2U(DPST), 2W(DPDT) |
| --- | --- | --- |
| Contact Material | AgNi AgSnO2 |
| Contact Rating (resistive) | 2A,2C:10A/120VAC,28VDC | 2U,2W:2x10A/120VAC, 28VDC |
| Max. Switching Power | 280W 1200VA |
| Max. Switching Voltage | 75VDC 380VAC | Max. Switching Current:10A |
| Contact Resistance or Voltage drop | ≤50mΩ | Item 4.12 of IEC 61810-7 |
| Operation life | Electrical | 105 | Item 4.30 of IEC 61810-7 |
|  | Mechanical | 107 | Item 4.31 of IEC 61810-7 |

■ OPERATION CONDITION

| Insulation Resistance | 100M Ω Min. at 500VDC | Item 7 of IEC 61810-5 |
| --- | --- | --- |
| Dielectric Strength Between Contacts Between Contact and coil | 50Hz 750V 50Hz 1500V | Item 6 of IEC 61810-5 Item 6 of IEC 61810-5 |
| Shock Resistance | 100m/s2 11ms | IEC68-2-27 Test Ea |
| Vibration Resistance | 10~40Hz double amplitude 1.27mm | IEC68-2-6 Test Fc |
| Terminals Strength | 10N | IEC68-2-21 Test Ua 1 |
| Solderability | 235℃±2℃ 3±0.5s | IEC68-2-20 Test Ta method 1 |
| Ambient Temperature | -40~105℃ |
| Relative Humidity | 85% (at 40℃) | IEC68-2-3Test Ca |
| Mass | Approx 10g |

■ ORDERING INFORMATION

■ COIL DATA

| Nominal Coil Voltage | Coil Voltage VDC Rated MAX | Coil Resistance Ω±10% | Pickup Voltage VDC(MAX) （75% of rated Voltage) | Release voltage VDC(min) (10% of rated Voltage) | Coil power Consumption W | Operate Time ms | Release Time ms |
| --- | --- | --- | --- | --- | --- | --- | --- |
| 3 | 3.9 | 9x2 | 2.25 | 0.3 | 2x1.0 | ≤10 | ≤5 |
| 5 | 6.5 | 25x2 | 3.75 | 0.5 |  |  |  |
| 6 | 7.8 | 36x2 | 4.50 | 0.6 |  |  |  |
| 9 | 11.7 | 85x2 | 6.75 | 0.9 |  |  |  |
| 12 | 15.6 | 145x2 | 9.00 | 1.2 |  |  |  |
| 18 | 23.4 | 324x2 | 13.5 | 1.8 |  |  |  |
| 24 | 31.2 | 576x2 | 18.0 | 2.4 |  |  |  |

CAUTION: 1). The use of any coil voltage less than the rated coil voltage will compromise the operation of the relay.

2). Pickup and release voltage are for test purposes only and are not to be used as design criteria.

■REFERENCE DATA

■ OVERALL AND MOUNTING DIMENSIONS

NOTES: 1). Dimensions are in millimeters.

2). Inch equivalents are given for general information only.

# Text boxes

#### RF2