| RG Relays |  |
| --- | --- |
| ● 30A switching Capability ● Ambient tem.-40°C to 125°C ● 1form A and 1form C Contacts ● Sealed and Covered structure ●With Transient Suppression resistor ●Contact gap min.0.6mm |  |

1．CONTACT DATA

| Contact Rating | Load Version | 1C | 1A |
| --- | --- | --- | --- |
|  |  | N.O. | N.C. | N.O. |
|  | Standard 12V | Res. load | on | 20A | 10A | 30A |
|  |  |  | off | 20A | 10A | 30A |
|  |  | Motor | on | 40A | 20A | 40A |
|  |  |  | off | 20A | 10A | 20A |
|  |  | Lamp | on | 120A | 40A | 120A |
|  |  |  | off | 20A | 10A | 20A |
|  | Powerful 24V | Res. load | on | 20A | 10A | 20A |
|  |  |  | off | 20A | 10A | 20A |
|  |  | Motor | on | 38A | 28A | 38A |
|  |  |  | off | 15A | 6A | 15A |
|  |  | Lamp | on | 70A | - | 70A |
|  |  |  | off | 7A | - | 7A |
| Contact Material | AgNi, AgSnO |
| Max Switching Voltage | 27VDC |
| Max Switching Current | 30A |
| Max Switching Power | 540W |
| Contact Resistance | 50m ohm (1A 24VDC) |
| Contact voltage drop | Typical. 100mV, max. 250mV (Rated Loading) |
| Life Expectancy Electrical | 100,000 Operations (at 30 Operations / minute) |
| Mechanical | 10,000,000 Operations |

2．OPERATION CONDITION

| Insulation Resistance | 100M ohm at 500VDC |
| --- | --- |
| Dielectric Strength | 500Vrms 1 min. |
| Operate Time | 10ms |
| Release Time | 10ms |
| Temperature Range | -40°C to 125° |
| Shock Resistance | 196 m/s2 (20g) |
| Vibration Resistance | 10-550Hz,49m/s2 (5g) |
| Termination | QC, PCB |
| Weight | Approx 22g |
| Construction | Covered, Sealed |

3．COIL PARAMETER

| Nominal Voltage (VDC) | Coil Resistance at20±10%(Ω) | Max Operate Voltage (VDC) | Min Release Voltage (VDC) | Parallel resistor ohm |
| --- | --- | --- | --- | --- |
|  | 1.4W | 1.8W |  |  |  |
| 12 | 90 | 124 | 7.2 | 1.2 | 680 |
| 24 | 360 | 1,800 | 14.4 | 2.4 | 1,800 |

4．ORDERING INFORMATION

5. dimensions (Unit: mm)