►FEATURE

| 30A 13.5VDC switching rating 40A inrush at 13.5VDC Confirm to RoHs,ELV directive | Size (mm) : 13.2 x 12 x 9.8 |  |
| --- | --- | --- |

►CONTACT  DATA

| Contact form | 1A | 1C |
| --- | --- | --- |
| Contact Material | Silver alloy |
| Load | Resistive load(COS phi=1) Cut 13.5VDC |
| Minimum load | 0.5A 12VDC |
| Max Switching Current | 40A |
| Max Switching Power | 420W |
| Contact Resistance | 100m ohm Max. at 6VDC 1A |
| Mechanical Life Expectancy | 10,000,000 Operations (At 300 operations/minute) |
| Contact rating | Load Type | Current(A) | Frequency ops/min | Duty Cycle | Life Expectancy |
|  |  | NO | NC |  |  |  |
|  | Resistive Load | 20 | - | 15 | 0.5 | 3 X 105 |
|  | Wiper reserve L=1.0mH | Make | 25 | 25 | 15 | 0.5 | 3 X 105 |
|  |  | Break | 5 | 5 |  |  |  |
|  | Motor reserve blocked L=0.77mH | 20A Inrush | 15 | 0.5 | 1 X 105 |
|  | Flasher Unit | 3x21W | - | 80 | 0.5 | 2 X 106 |
|  | Lamp | Inrush | 100 | - | 6 | 1/6 | 1 X 105 |
|  |  | Steady | 10 | - |  |  |  |

►CHARACTERISTICS  DATA

| Insulation Resistance | 100MΩ min (at 500VDC) |
| --- | --- |
| Dielectric Strength Between | Open Contacts | 500VAC (For one minute) |
|  | Coil & Contacts | 500VAC (For one minute) |
| Operate time(At nomi. Volt.) | 4ms |
| Release Time(At nomi. Volt.) | 2ms |
| Ambient Temperature | - 40 to 105°C |
| Shock Resistance | 6msec up to 30g (No change in the switching state>10 micro sec) |
| Max. switching frequency | Mechanical : 18,000 operations/hr |

| Humidity | 20-50% |
| --- | --- |
| Weight | Approx. 4g |

►COil data

| Nominal Voltage | 6 | 12 | 24 | 0.57W |
| --- | --- | --- | --- | --- |
| Coil Resistance | 63 | 254 | 1,010 |  |
| Rated Current | 95 | 47.5 | 23.7 |  |
| Max. Operate Voltage | 3.45 | 6.9 | 13.8 |  |
| Max. Release Voltage | 0.6 | 1.2 | 2.4 |  |
| Nominal Voltage | 6 | 12 | 24 | 0.80W |
| Coil Resistance | 45 | 180 | 720 |  |
| Rated Current | 133.3 | 66.7 | 33.3 |  |
| Max. Operate Voltage | 3.45 | 6.9 | 13.8 |  |
| Max. Release Voltage | 0.6 | 1.2 | 2.4 |  |
| Max. Applicable Voltage | 130% At 70°C, 170% At 23°C |

►ORDERING  INFORMATION

► ENGINEERING  DATA

►OVERALL AND MOUNTING DIMENSIONS

# Text boxes

#### RP