Handouk

►FEATURE

● 30A switching capabilities

● DPST-NO and DPDT configurations

● Meets 8mm creepage distance,4KV dielectric

● Dust cover or sealed version;PCB or QC terminal

►CONTACT DATA

| Contact Arrangement | 2A | 2C |
| --- | --- | --- |
| Initial Contact Resistance | 50mΩ(at 1A 6VDC) |
| Contact Material | AgCdO |
| Contact Ratings | NC: 3A 28VDC/277VAC / NO:30A 120/277AC;20A 28VDC |
| Max Switching Voltage | 277VAC/30VDC |
| Max Switching Current | 30A |
| Max Switching Power | 8,310VA / 560W |
| Life Expectancy | Electrical | 100,000 Ops (30A 250VAC) at 30 Operations / minute |
|  | Machanical | 5,000,000 Operations |

►OPERATION CONDITION

| Insulation Resistance | 1000MΩMin at 500VDC |
| --- | --- |
| Dielectric Strength Between | Open Contacts | 1,500Vrms 1min. |
|  | Contact poles | 2,000Vrms 1min. |
|  | Contacts and coil | 4,000Vrms 1min. |
| Surge voltage between contacts and coil | 10,000VAC |
| Operate Time | 15ms |
| Release Time | 10ms |
| Temperature Range | -40℃to+75℃ |
| Shock Resistance | Operating Extremes | 100m/s2 |
|  | Damage Limits | 1000m/s2 |
| Vibration Resistance | DA 1.65mm,10 to 55Hz |
| Humidity | 35 to 85%,+40℃ |
| Weight | Approx. 86g. |
| Construction | Dust cover and Sealed |
| Termination | Panel Mount QC |

►ORDERING INFORMATION

►COIL PARAMETER

VDC

| Nominal Voltage VDC | Pick-up Voltage VDC | Drop-out Voltage VDC | Max. allowable Voltage VDC (at 20℃) | Coil Resistance Ω |
| --- | --- | --- | --- | --- |
| 5 | 3.8 | 0.5 | 5.5 | 15.3±10% |
| 6 | 4.5 | 0.6 | 6.6 | 22±10% |
| 12 | 9 | 1.2 | 13.2 | 86±10% |
| 24 | 18 | 2.4 | 26.4 | 350±10% |
| 48 | 36 | 4.8 | 52.8 | 1390±10% |
| 110 | 83 | 11 | 121 | 7255±10% |

VAC

| Nominal Voltage VAC | Pick-up Voltage VAC | Drop-out Voltage VAC | Max. allowable Voltage VAC (at 20℃) | Coil Resistance Ω |
| --- | --- | --- | --- | --- |
| 24 | 19.2 | 4.8 | 26.4 | 45±10% 50Hz |
| 120 | 96 | 24 | 132 | 1125±10% 50Hz |
| 208 | 166.4 | 41.6 | 228.8 | 3380±10% 50Hz |
| 220 | 176 | 44 | 242 | 3800±10% 50Hz |
| 240 | 192 | 48 | 264 | 4500±10% 50Hz |
| 277 | 221 | 55.4 | 304.7 | 6000±10% 50Hz |

►DEMENSIONS(mm)

►CHARACTERISTICS CURVE

# Text boxes

#### GD