Handouk

►FEATURES

● 5A 250VAC 300,000 switching capabilities

● SPST-NO and SPDT configurations

● Subminiature, standard PCB layout

Size (L x W x H)

20.5 x 10.6 x 15.3mm

►CONTACT DATA

| Contact Form | 1A | 1C |
| --- | --- | --- |
| Contact Material | Silver alloy |
| Contact Ratings | 5A 250VAC 5A 30VDC 10A 125VAC | NO | NC |
|  |  | 5A 250VAC 5A 30VDC 10A 125VAC | 3A 250VAC 3A 30VDC |
| Contact resistance | 100mΩ Max at 24VDC 1A |
| Max. Switching Voltage | 277VAC / 30VDC |
| Max. Switching Current | 10A | 3A |
| Max. Switching Power | 1250VA / 150W | 750VA / 90W |
| Nominal coil power | Standard:0.45W, Sensitive:0.2W |
| Life Expectancy | Electrical | 100,000 Operations (at 30 ops a minute) |
|  | Mechanical | 10,000,000 Operations |

►OPERATION CONDITION

| Insulation Resistance | 1000M ohm min (at 500VDC) |
| --- | --- |
| Dielectric Strength | Between open Contacts | 1,000VAC (For one minute) |
|  | Between coil & Contacts | 4,000VAC (For one minute) |
| Surge Voltage between Contacts and coil | 8000V (at 1.2X50us) |
| Operate time | 8ms |
| Release Time | 5ms |
| Shock resistance | Operating Extremes | 100m/s2 |
|  | Damage Limits | 1,000m/s2 |
| Vibration resistance | 1.6mm, 10 to 55Hz |
| Humidity | 35~95% |
| Temperature Range | -40 ~ 70℃ |
| Weight | Approx 7g |
| Safety Standard (UL) | E197546 |

►COIL PARAMETER

| Nominal Voltage (VDC) | Max Operate Voltage | Min. Release Voltage | Max. Applicable Voltage | Coil Resistance at 20 C (Ω) |
| --- | --- | --- | --- | --- |
|  |  |  |  | Standard (1A, 1C) | Sensitive ( 1A ) |
| 3 | 2.25 | 0.15 | 3.9 | 20+/-10% | 45+/-10% |
| 5 | 3.75 | 0.25 | 6.5 | 55+/-10% | 125+/-10% |
| 6 | 4.5 | 0.3 | 7.8 | 80+/-10% | 180+/-10% |
| 9 | 6.75 | 0.45 | 11.7 | 180+/-10% | 400+/-10% |
| 12 | 9.0 | 0.6 | 15.6 | 320+/-10% | 720+/-10% |
| 18 | 13.5 | 0.9 | 23.4 | 720+/-10% | 1600+/-10% |
| 24 | 18 | 1.2 | 31.2 | 1280+/-10% | 2800+/-10% |
| 48 | 36 | 2．4 | 62．4 | 5120+/-10% |  |

►ORDERING INFORMATION

►DIMENSIONS  (Unit: MM)

►USEFUL CURVE

# Text boxes

#### HF