HANDOUK

| ■ FEATURES |  |
| --- | --- |
| 1 Form A (W + AgSnO2) | 1 A, 1C, 2A,2C |  |
| ● Special contact struction ● Incandescent lamp load: 3,500W 277VAC ● 5kV dielectric (Between coil and contacts) ● Creepage 11mm-NO ● VDE 0700, 0631 insulation ● IEC60335-1, EN60669-1 ● Low height: 15.7mm ● Latching relay | ● 20A(1A,1C) 10A(2A,2C) switching capabilities ● 5kV dielectric (Between coil and contacts) ● Creepage 11mm-NO 10mm-CO version ● VDE 0700, 0631 insulation ● IEC60335-1 ● UL File No. E222977 |  |

■ CONTACT DATA

| Contact arrangement | 1 Form A (Special contact) | 1A, 1C | 2A, 2C |
| --- | --- | --- | --- |
| Contact resistance1) | 100mΩ max.(at 1A 6VDC) | 100mΩ max.(at 1A 6VDC) | 100mΩ max.(at 1A 6VDC) |
| Contact material | W + AgSnO2 | AgSnO2 | AgSnO2 |
| Contact rating(Res.Load) | 16A 250VAC | 16A 250VAC | 8A 250VAC |
| Typ. applicable load | Incandescent Lamp: 3,500W 277VAC Inrush current:165A/20ms | Incandescent Lamp: 1,500W 277VAC | Lamp: Tungsten 3A 277VAC |
|  | LED(Electronic ballast):492A/1.5ms | Standard ballast: 8A 277VAC Electronic ballast:5A 120VAC | Standard ballast: 3A 277VAC |
| Max. switching voltage | 480VAC | 480VAC / 300VDC | 440VAC / 300VDC |
| Max. switching current | 16A | 20A | 10A |
| Max. switching power | 4,000VA | 4,000VA | 2,000VA |
| Mechanical endurance | 2 x 106 operations | 2 x 106 operations | 2 x 106 operations |
| Electrical endurance | 1.2 x 104 ops (3,500W 277VAC, Tungsten lamp, at 40°C, 1s on 9s off) 6 x 103 ops (16A 250VAC, Resistive load, at 85°C, 5s on 5s off) | 5 x 104 ops (NO:16A 250VAC, Resistive load, at 85°C, 1s on 9s off) | 2A Type: 5 x 104 ops (8A 250VAC, General use, at 85°C, 5s on 5s off) 2C Type: 2 x 104 ops (8A 250VAC, General use, at 85°C, 5s on 5s off) |

Notes: 1) The data shown above are initial values.

■ CHARACTERISTICS

| Insulation resistance | 1,000MΩ (At 500VDC) |
| --- | --- |
| Dielectric strength | Between coil & contacts | 5,000VAC 1min. |
|  | Between open contacts | 1,000VAC 1min. 1,250VAC (W + AgSnO2) |
|  | Between contact sets | 2,500VAC 1min. (2 poles) |
| Surge voltage(Between coil & contacts) | 10kV (1.2 / 50µs) |
| Set time (at rated. Volt.) | 10ms max. |
| Reset time (at rated. Volt.) | 10ms max. |
| Temperature rise (at rated volt.) | 55K max. (W + AgSnO2) |
| Shock resistance * | Functional | 98m/s2 |
|  | Destructive | 980m/s2 |
| Vibration resistance* | 10Hz to 150Hz 10g/5g |
| Humidity | 5% to 85% RH |
| Ambient temperature | -40°C to 85°C |
| Termination | PCB |
| Unit weight | Approx. 13.5g |
| Construction | Plastic sealed, Flux proofed |

Notes: 1) The data shown above are initial values. 2) * Index is not in relay length direction.

■ COIL POWER

| Coil Power | 1 Coil Latching | Approx. 400mW |
| --- | --- | --- |
|  | 2 Coil Latching | Approx. 600mW |

■ COIL DATA                                                                                 ( at 20℃ )

| Nominal Voltage VDC | Set/Reset Voltage VDC max.1) | Pulse Width (ms) | Max. Voltage VDC | Coil Resistance Ω |
| --- | --- | --- | --- | --- |
|  |  | Typical | Min. |  |  |
| One Coil Latching, 0.4W |
| 5 | 3.5 | ≥50 | 30 | 6 | 62 ± 10% |
| 6 | 4.2 | ≥50 | 30 | 7.2 | 90 ± 10% |
| 9 | 6.3 | ≥50 | 30 | 10.8 | 202 ± 10% |
| 12 | 8.4 | ≥50 | 30 | 14.4 | 360 ± 10% |
| 24 | 16.8 | ≥50 | 30 | 28.8 | 1,440 ± 10% |

| Nominal Voltage VDC | Set/Reset Voltage VDC max.1) | Pulse Width (ms) | Max. Voltage VDC | Coil Resistance Ω |
| --- | --- | --- | --- | --- |
|  |  | Typical | Min. |  |  |
| Two Coil Latching, 0.6W |
| 5 | 3.5 | ≥50 | 30 | 7.5 | 42 ± 10% |
| 6 | 4.2 | ≥50 | 30 | 9 | 55 ± 10% |
| 9 | 6.3 | ≥50 | 30 | 13.5 | 135 ± 10% |
| 12 | 8.4 | ≥50 | 30 | 18 | 240 ± 10% |
| 24 | 16.8 | ≥50 | 30 | 36 | 886 ± 10% |

Notes: 1) The data shown above are initial values. 2) Maximum voltage refers to the maximum voltage which relay coil could endure in a short period of time.

■ SAFETY APPROVAL RATINGS

| UL/CUL | One Pole | 16A/20A 250VAC 85℃, 1HP 240VAC 40℃, TV-8 240VAC 40℃, TV-12 120VAC 40℃(1 form A), Tungsten 360W 125VAC 40℃(1 Form A), Tungsten 1,920W 8A 240VAC 40℃, Tungsten 12A 120VAC 40℃, Standard ballast 16A 120VAC 40℃, Standard ballast 8A 277VAC 40℃, Standard ballast 5A 347VAC/480VAC 40℃, Electronic ballast 5A 120VAC 40℃ |
| --- | --- | --- |
|  | Two Poles | 10A/8A 250/277VAC General use at 85℃, 1/2HP 240VAC at 40℃ Standard ballast 3A 277VAC at 40℃, Tungsten Lamp 3A 277VAC at 40℃ |

| UL/CUL | One Pole(1AT) (Special contact) | 16A/20A 250VAC General use at 85℃, Standard ballast 2A 347/480VAC at 60℃, Standard ballast 5A 277VAC at 40℃, Electronic ballast 2A 347/480VAC 60℃, Electronic ballast 16A 120/277VAC at 40℃, 3,500W 277VAC Tungsten Lamp at 40℃, TV-15 120VAC 40℃, Tungsten 15A 120VAC 40℃ |
| --- | --- | --- |

■ ORDERING CODE

Notes; 1) We recommended flux proofed types for a clean environment (free from contaminations like H2S,SO2,NO2,dust,etc)

We suggest to choose plastic sealed types and validate it in real application for an unclean environment(with contaminations

Like H2S,SO2,NO2,dust,etc)

2) Contact is recommended for suitable condition and specifications if water cleaning or surface process is involved in

assembling relays on PCB.
     3) The customer special requirement express as special code after evaluating by HANDOUK. E.g.(335) stand for product in

accordance to IEC 60335-1 (GWT).

4) Two packing methods available:plastic tray package, tube package, Standard tube lenghth 616mm. Any special requirement

needed, please contact us for more details.

5) For products that should meet the explosion-proof requirements of  “IEC60079” series, please note (Ex) after the

specification while placing orders. Not all products have explosion-proof certification, so please contact us if necessary,

in order to select the suitable products.

■ OUTLINE DIMENSIONS, WIRING DIAGRAM AND PC BOARD LAYOUT          Unit : mm

Remark: 1) In case of no tolerance shown in outline dimension: outline dimension ≤1mm, tolerance should be ±0.2mm; outline dimension 〉1mm and ≤5mm, tolerance should be ±0.3mm; outline dimension 〉5mm, tolerance should be ±4mm.

2) The tolerance without indicating for PCB layout is always ±0.1mm.

3) The width of the gridding is 2.52mm.

1. Relay is on the "reset" status when being released from stock, with the consideration of shock, with the 
consideration of shock risen from transit and relay mounting, relay would be changed to "set" or "reset" status, 
therefore, when application (connecting the power supply), please reset the relay to "set" or "reset" status on request.

2. In order to maintain "set" or "reset" status, energized voltage to coil should reach the rated voltage, impulse width
should be 5 times more than "set" or "reset" time. Do not energize voltage to "set" coil and "reset" coil simultaneously. 
And also long energized time ( more than 1 min.) should be avoided.

3.Keep the product away from strong magnetic field during transportation, storage and application, to avoid change of set/reset voltage.

Disclaimer

The specification is for reference only. Specifications subject to change without notice.

We could not evaluate all the performance and all the parameters for every possible application. Thus the use should be in a right position to choose the suitable product for their own application. If there is any query, please contact HANDOUK for technical service. However, it is the user’s responsibility to determine which product should be used only.

Handouk Electronics Co.,Ltd. All rights of HANDOUK are reserved.

Handouk Electronics Co., Ltd                                           EMAIL:sales@handouk.co.kr

# Text boxes

#### HL2-1(2pin)-L