Handouk

►FEATURES

| * 10A switching capabilities * 5KV dielectric coil to contacts * Low height 12.5 mm * Sealed IP67 & Flux proof types available * Creepage distance > 8mm | * Socket available * Size (L x W x H) 28.5x10.1 x12.5mm |  |
| --- | --- | --- |

►CONTACT DATA

| Contact Arrangement | 1A, 1B, 1C |
| --- | --- |
| Contact Material | See ordering info. |
| Contact Resistance 1) | 100m ohm max at 1A 6VDC (Initial) |
| Contact Ratings(Resistance Load) | 10A 250VAC / 30VDC |
| Max Switching Voltage | 440VAC / 300VDC |
| Max Switching Current | 10A |
| Max Switching Power | 2,500VA 300W |
| Life expectancy | Electrical | 100,000 operations ( 8A 250VAC, Resistive load, AgNi at 85ºC 5s on, 5s off) |
|  | Mechanical | 10,000,000 operations |

Notes: 1) The data shown above are initial values.

►OPERATION CONDITION

| Insulation Resistance (Initial) | 1,000MΩ Min (at 500VDC) |
| --- | --- |
| Dielectric Strength Between | Open Contacts | 1,000VAC (for one minute) |
|  | Contacts and Coil | 5,000VAC (for one minute) |
| Surge voltage (Between coil & contacts) | 10kV ( 1.2/50µs) |
| Operate Time (at nomi. Volt.) | Max. 10ms |
| Release time (at nomi. Volt.) | Max. 5ms |
| Temperature rise (at nomi.Volt.) | 55K max. |
| Shock Resistance* | Functional | NC : 49 m/s2 | NO : 98 m/s2 |
|  | Destructive | 980 m/s2 |
| Vibration Resistance* | NC (no coil voltage) | DA : 0.8mm, 10 to 55Hz |
|  | NO | DA : 1.65mm, 10 to 55Hz |
| Ambient temperature | -40ºC ~ +85ºC |
| Humidity | 5 - 85% RH |
| Construction | Plastic sealed IP67 & Flux proof |
| Unit Weight | Approx. 8g |
| Termination | PCB |
| UL No.(E222977) AgNi, AgNi+Au | Version 1,3,5,61) : 10A 250VAC at 85ºC 10A 30VDC at 85 ºC B300 at 85 ºC, R300 at 85 ºC 1/2HP 240VAC at 85 ºC AgSnO2:1/3HP 120VAC at 85 ºC |

Notes: * index is not in relay length direction.
1) All values unspecified are at room temperature. Only typical loads are listed above. Other load specifications can be available upon requested.

►COIL PARAMETER

| Nominal Voltage VDC | PicK-up Voltage VDC max1) | Drop-out Voltage VDC min1) | Max allowable Voltage VDC(at 20ºC) 2) | Current mA | Coil resistance ohm | Coil Power mW |
| --- | --- | --- | --- | --- | --- | --- |
| 5 | 3.50 | 0.50 | 7.5 | 44 | 113± 10% | 220 ~ 290 |
| 6 | 4.20 | 0.60 | 9.0 | 36 | 164± 10% |  |
| 9 | 6.30 | 0.90 | 13.5 | 25 | 360± 10% |  |
| 12 | 8.40 | 1.20 | 18.0 | 19.35 | 620± 10% |  |
| 18 | 12.70 | 1.80 | 27.0 | 13.89 | 1,295± 10% |  |
| 24 | 16.80 | 2.40 | 36.0 | 10.21 | 2,350± 15% |  |
| 483) | 33.60 | 4.80 | 72.0 | 6 | 8,000 ± 15% |  |
| 603) | 42.00 | 6.00 | 90.0 | 4.8 | 12,500 ± 15% |  |

Notes: 1) The data shown above are initial values.
2) Maximum voltage refers to the maximum voltage which relay coil could endure in a short period of time.
3) For products with rated voltage ≥48V, measures should be taken to prevent coil overvoltage in order to protect coil in test and application (eg. Connect diodes in parallel).

►ORDERING INFORMATION

Notes: 1) we recommend plastic sealed types and validate it in real application for an unclean environment(with contaminations like H2S
SO2,NO2,duct,etc). we suggest to choose flux proofed types for a clean environment (free from contaminations like H2S, SO2,NO2,duct,etc)
2) Contact is recommended for suitable condition and specifications if water cleaning or surface process is involved in assembling relays on PCB. 3) For gold plated type, the min. switching voltage is 10mA 5VDC. 4) The customer special requirement express as special code after evaluating by Handouk. e.g. (335) stands for product in accordance to IEC60335-1 (GWT); e.g.(253) stands for Reflow soldering version. 5) Standard tube packing length is 600mm. Any special requirement needed, please contact us for more details. 6) For products that should meet the explosion-proof requirements of IEC60079 series. Please note (Ex) after the specification while placing orders. Not all products have explosion-proof certification, so please contact us if necessary, in order to select the suitable products.

►Outline dimensions, wiring diagram and pc board layout

►CHARACTERISTICS CURVE

►Relay Sockets

|  | Features * The Dielectric strength can reach 5,000VAC and the insulation resistance is 1,000MΩ * Two mounting types are available : PCB and screw mounting. * Environmental friendly product (RoHS compliant) |
| --- | --- |

►CHARACTERISTICS

| Type | Nominal voltage | Nominal current | Ambient Temperature | Dielectric Strength min. | Unit weight |
| --- | --- | --- | --- | --- | --- |
| HL51-1C-A1-1 | 250VAC | 10A | -40ºC ~ +85ºC | 5,000VAC | Approx.3g |
| HL51-2C-A1 | 250VAC | 10A | -40ºC ~ +85ºC | 5,000VAC | Approx.3g |

►Outline dimensions, wiring diagram and pc board layout

Things to be noticed when selecting sockets :

1.Please choose suitable relay socket according to the actual mounting environment, relay contact poles and terminal layout. If there is any query on selection, please contact Handouk for the technical service. 2.As for related components, they should be selected separately. Please do give clear indication of the types of relay sockets and related components you choose while placing order. 3. The above is only an example of typical socket and related component type which is suitable to HL51 1 poles relay. If you have any special requirements, please contact us. 4. Main outline dimension, outline dimension 〉50mm, tolerance should be ±1mm; 20mm 〈 outline dimension ≤50mm, tolerance should be ±0.5mm; 5mm 〈 outline dimension ≤ 20mm, tolerance should be ±0.4mm; outline dimension ≤ 5mm, tolerance should be ±0.3mm.

# Text boxes

#### HL51