HANDOUK

►FEATURES

● 5A switching capabilities

● 1 pole configurations

● 3KV dielectric strength(between coil to contacts)

●Slim size(width 5mm, height 12.5mm)

●High sensitivity min.0.12W

Size (L x W x H)

20 x 5 x 12.5mm

►CONTACT DATA

| Contact Form | 1A (SPST) |
| --- | --- |
| Contact Ratings | 5A 30VDC / 5A 250VAC |
| Max. Switching Voltage | 250VAC / 30VDC |
| Max. Switching Current | 5A |
| Max. Switching Power | 1,250VA / 150W |
| Contact Resistance(At 1A 6VDC)1) | Gold plated : 50mΩ, Non-Gold plated : 100mΩ |
| Min. contact load 2) | Gold plated : 1mA 5VDC , Non-Gold plated : 10mA 5VDC |
| Life Expectancy | Electrical | 100,000 Operations (3A 250VAC/30VDC, Resistive load, AgNi, at 85(C,1s on 9s off) 50,000 Operations (5A 250VAC/30VDC, Resistive load, AgNi, room temp., 1s on 9s off) |
|  | Mechanical | 20,000,000 Operations |

Notes:1)T	he data shown above are initial values. 2)Min.contact load is reference value. Please perform the confirmation test with the actual load before usage since reference value may change according to switching frequencies,environmental conditions and expected life cycles.

►OPERATION CONDITION

| Insulation Resistance | 1000MΩ min (at 500VDC) |
| --- | --- |
| Dielectric Strength | Between open Contacts | 1,000VAC (For one minute) |
|  | Between coil & Contacts | Standard(HS/HAS) : 2,000VAC (For one minute) Hi-Dielectric(HSD/HSDA) : 3,000VAC (For one minute) |
| Surge Voltage (between Contacts and coil)4) | 6kV (1.2x50us) |
| Operate time (at nominal volt.) | 10ms |
| Release Time (at nominal volt.) | 5ms |
| Temperature rise (at nomi.Volt.) | 45(C |
| Shock resistance | Operating Extremes | 98 m/s2 |
|  | Damage Limits | 980 m/s2 |
| Vibration resistance | 10~55Hz 1.5mm Double amplitude |
| Humidity | 5~85% |
| Temperature Range | -40 ~ 85(C |
| Weight | Approx 3g |
| Coil power | 0.12 to 0.18W |

Notes:1) the data shown above are initial values. 2)Please find coil temperature curve in the characteristic curves below. 3)UL insulation system:Class F, Class B, Class A. 4) Contact refers to the mov.-contact.

►COIL PARAMETER

| Nominal Voltage (VDC) | Coil Resistance (at 20(C (Ω) | Coil Current (at 20℃)mA | Max Operate Voltage2) | Min. Release Voltage2) | Max. Applicable Voltage3) |
| --- | --- | --- | --- | --- | --- |
| 5 | 208±10% | 24.0 | 3.50 | 0.25 | 6.0 |
| 6 | 300±10% | 20.0 | 4.20 | 0.30 | 7.2 |
| 9 | 675±10% | 13.0 | 6.30 | 0.45 | 10.8 |
| 12 | 1200±10% | 10.0 | 8.40 | 0.60 | 14.4 |
| 18 | 2700±15% | 6.70 | 12.6 | 0.90 | 21.6 |
| 244) | 3200±15% | 7.50 | 16.8 | 1.20 | 28.8 |

Notes:1)All above data are tested when the relays terminals are downward position. Other positions of the terminals, the pick-up and drop-out voltages will have ±5% tolerance. For example, when the relay terminals are transverse position, the max. pick-up voltage change is 75% of norminal voltage. 2)The data shown above are initial values. 3)Maximum voltage refers to the maximum voltage which relay coil could endure in a short period of time. 4)24VDC 120mW type are also available, please see ordering information for more details.

►SAFETY APPROVAL RATINGS

| UL/CUL | Single contact | AgSnO2 | 3A 250VAC cosØ=1 at 85(C 3A 30VDC L/R=0ms at 85(C |
| --- | --- | --- | --- |
|  |  | AgNi | 5A 250VAC cosØ=1 5A 30VDC L/R=0ms |
|  | Bifurcated contact | AgNi | 3A 250VAC cosØ=1 at 85(C 3A 30VDC L/R=0ms at 85(C 5A 250VAC cosØ=1 5A 30VDC L/R=0ms |

Notes:1)All values unspecified are at room temperature. 2)Only typical loads are listed above. Other load specifications can be available upon request.

►ORDERING INFORMATION

►DIMENSIONS  (Unit: MM)

►USEFUL CURVE

Test conditions: AgNi,                   TEST CONDITIONS:

Resistive load, 250VAC/30VDC          5A 85(C (Typical curve

Room temp., 1s on 9s off.                of 24VDC standard type)

►RELAY Socket

|  | ● Ambient temperature : -40(C ~ 70(C ● Rated voltage: 250VAC ● Rated current: 5A (Each pole) ● Dielectric strength: 3,000VAC min.(Between I/O) ● Remove the relay card: HS-B ● Retainer: HS-Socket, HAS-Socket |
| --- | --- |

►DIMENSIONS  (Unit: MM)

# Text boxes

#### HSD / HSDA