■ FEATURES

| ● Only impulse excitation is needed, both for single and double coil. ● Low power consumption with great load capability. ● Accessories can be welded upon customers’ requirement ● Dimensions:(82X66X30)mm |  |
| --- | --- |

■ CONTACT  PARAMETER

| Contact form | 1B/2B |
| --- | --- |
| Contact material | Silver alloy |
| Contact resistance | Max.10mΩ(1A 6VDC) |
| Contact rating (resistive load) | 200A 250VAC |
| Max. Switching Voltage | 250VAC |
| Max. Switching Current | 200A |
| Max. Switching Power | 50KVA |
| Life | Mechanical life | 5X105 ops |
|  | Electrical life | 5X103 ops |
| Max. Short-circuit current |  |

■ CHARACTERISTICS

| Insulation resistance | 1000MΩ Min.(500VDC) |
| --- | --- |
| Dielectric strength | Coil & contact | 4,000 VAC 50/60Hz 1min |
|  | Between open contacts | 2,000 VAC 50/60Hz 1min |
|  | Between contacts | 4,000 VAC 50/60Hz 1min |
| Operate Time | 60ms Max. |
| Release Time | 60ms Max. |
| Relative humidity | 45%-90%RH |
| Ambient temperature | -40℃~+70℃ |
| Impulsion | 98m/s2 |
| Vibration | 10-55HZ,1.5mm |
| Weight(without accessories) | 450g |

COIL DATA

| Rated coil (VDC) | Coil resistance (Ω)±10% | Coil power(W) | Operate voltage (VDC) | Release voltage (VDC) | Over voltage (VDC) | Impulse Duration (ms) |
| --- | --- | --- | --- | --- | --- | --- |
|  | Single coil | Double coil | Single coil | Double coil |  |  |  |  |
| 9 | 32.4 | 16.2/16.2 | 8.5 | 17.0 | ≤75% | ≤75% | ≤150% | ≥180ms |
| 12 | 57.6 | 28.8/28.8 |  |  |  |  |  |  |
| 24 | 230.4 | 115/115 |  |  |  |  |  |  |
| 48 | 271 | 135/135 |  |  |  |  |  |  |
| 100 | 1176 | 588/588 |  |  |  |  |  |  |

Notes: When requiring other nominal voltage, special order allowed.

Ordering information

■ 2B DIMENSION、WIRING DIAGRAM（Unit：mm）

Note: No tolerance marked. When dimension is ≤1mm, the tolerance shall be±0.2mm; when dimension is 1-5mm, the

tolerance shall be±0.3mm; when dimension is >5mm, tolerance should be ±0.5mm.

■ 1B DIMENSION、WIRING DIAGRAM（Unit：mm）

■ TYPICAL APPLICATION

●Smart meter   ●electric remote control   ●power composite switch  ●leakage protection

■ Notice

1. The factory default of the contacts is to stay closure (reset), It’s possible that the status will be changed with be

changed with impact during shipment or installation. Please make sure the status of the contacts stay reset before using.

2. To guarantee the latching relay operates reliably, the excitation voltage to coil should meet the rated value and impulse

duration needs to exceed 3 times of the operation time. For double coil type latching relay, please neither apply voltage

signal to both coils at the same time nor apply with long time (over 1 min).

3. Latching relays without copper braided wires, the loaded PIN can neither be tin soldered nor be wrenched. Rigid fixing of

the two pins is also not allowed.

4. Magnetic latching relay is polarized relay. If customer needs different kinds of polarity from the data sheet,

please inform us.

5. Please handle the latching relays with cared during factory’s incoming-inspection and when put in use,

do not let the relay drops which will impact the parameter. Please make strict distinction between relay made for.

# Text boxes

HT25L