HANDOUK

■ FEATURES

| ●Magnetic Latching relay ● 200A switching capability ●Strong resistance ability to shock & vibration ●Heavy load up to 50K VA ●Environmental friendly product (RoHS compliant) ●Outline Dimensions(107.5 X 97.0 X 29.5)mm |  |
| --- | --- |

■ CONTACT  DATA

| Contact arrangement | 2A / 2B |
| --- | --- |
| Contact resistance | 1.0mΩ(at 1A 24VDC) |
| Contact material | AgSnO2, AgCdO |
| Contact Ratings(Res. load) | 200A 250VAC / 30VDC |
| Max Switching Power | 50,000VA |
| Mechanical endurance | 5 X 105 ops |
| Electrical endurance | 5 X 103 ops |

■ CHARACTERISTICS

| Insulation Resistance | 1,000MΩ( at 500VDC) |
| --- | --- |
| Dielectric Strength | Between coil& Contacts | 4,000VAC 1min |
|  | Between open& Contacts | 2,000VAC 1min |
| Operate Time(at nomi. volt) | 50ms max. |
| Release Time(at nomi. volt) | 50ms max. |
| Vibration Resistance | 10 Hz~ 55Hz 1.5mm DA |
| Shock Resistance | Destructive | 98m/s2 |
|  | Functional | 980m/s2 |
| Humidity | 98% RH, 40℃ |
| Ambient temperature | -40℃ to 70℃ |
| Termination | PCB& QC |
| Unit Weight | Approx .500g |
| Construction | Dust proofed |
| Coil power | Single Coil: 12W; Double Coil: 24 W |

■COIL DATA

| Nominal Voltage (VDC) | Pick-up Voltage VDC | Pulse Duration (ms) | Coil Resistance (Ω) +/-10% |
| --- | --- | --- | --- |
| 12 | 906 | ≥150 | Single Coil | 12 |
| 24 | 19.2 | ≥150 |  | 48 |
| 48 | 38.4 | ≥150 |  | 190 |
| 12 | 9.6 | ≥150 | Double Coils | 6+6 |
| 24 | 19.2 | ≥150 |  | 24+24 |
| 48 | 38.4 | ≥150 |  | 95+95 |

Notes: When requiring other nominal voltage, special order allowed.

NOTICE

- Relay is on the “set” status hen being released from stock, with the consideration of shock risen from transit and relay mounting, relay would be changed to “reset” status, therefore, when application(connecting the power supply), please reset the relay to “set” or “reset” status on request.

- In order to maintain “set” or “reset” status, energized voltage to coil should reach the rated voltage, impulse width should be 5 times more than “set” or “reset” time. Do not energize voltage to “set” coil and “reset” coil simultaneously. And also long energized time (more than 1 min) should be avoided.

- The terminals of relay without twisted copper wire can not be tin-soldered, can not be mover willfully, more over two terminals can not be fixed at the same time.

■ OUTLINE DIMENSIONS AND WIRING DIAGRAM                               Unit:mm

Remark: In case of no tolerance shown in outline dimension: outline dimension≤1mm,tolerance should be±0.2mm;

outline dimension〉1mm and ≤5mm,tolerance should be ±0.3mm；outline dimension >5mm ,tolerance should be± 0.4mm.

Remark: The polarity of Reverse polarity and Standard polarity is opposite.

Disclaimer

This datasheet is for the customers’ reference. All the specifications are subject to change without notice.

We could not evaluate all the performance and all the parameters for every possible application. Thus the user should be in a right position to choose the suitable product for their own application. If there is any query , please contact us for the technical service. However, it is the user’s responsibility to determine which product should be used only.

# Text boxes

HT6