Handouk Biotech

►FEATURES

● 2 From C contact, polarized relay

● High sensitivity 150mW

● Matching 16 pin IC socket

● High switching capacity 60W, 125VA

● Epoxy sealed for automatic wave soldering

and cleaning 16 pin IC socket

►CONTACT DATA

| Contact Arrangement | DPDT (2 Form C) |
| --- | --- |
| Initial Contact Resistance | 50m ohm |
| Contact Material | Ag-AuAg8, AgPd60 |
| Rated load (Res. Load) | 2A, 30VDC, 1A 125VAC |
| Max. switching power | 60W, 125VA |
| Max. switching Voltage | 220VDC, 250VAC |
| Max. switching current | 2A |
| Min. Applicable Load | 10mV 10 micro A |
| Electrical Life | 1 x 105 ops (2A 30VDC), 5 x 105 ops (1A 30VDC) |
| Mechanical Life | 1 x 108 ops |

►OPERATION CONDITION

| Initial Insulation resistance | 1000M ohm 500VDC |
| --- | --- |
| Operate time (nominal voltage) | Max. 4ms |
| Release time (nominal voltage) | Max. 3ms |
| Set time (Latching) | 3ms |
| Reset time(Latching) | 3ms |
| Bounce time | Max. 1.5ms |
| Dielectric strength | Coil and contacts | 1,500Vrms, 1min(1 coil) 1,000Vrms, 1min(2 coil) |
|  | Between contacts | 1,000Vrms, 1min |
| Vibration resistance | 196 m/s2(20g) 10 to 55Hz |
| Shock resistance | Functional | 490m/s2(50g) |
|  | Destructive | 980m/s2(100g) |
| Ambient temperature | -40°C~+85°C |
| Humidity | 5% to 85% R.H. |
| Capacitance between | Contacts | 2.0p |
|  | Contact sets | 1.5p |
|  | Contact to coil | 5.0p |
| Max. Solder Temp. Time | 270°C 5s |
| Max. Solvent Temp. Time | 80°C 30s |
| Termination | DIP & PCB |
| Unit weight | Approx. 4.5g |
| Construction | Sealed |

►COIL

| Coil power |  | Sensitive | Standard |
| --- | --- | --- | --- |
|  | Single side stable | 150mW | 200mW |
|  | Latching 2 coil | 150mW | 200mW |
|  | Latching 1 coil | 75mW | 100mW |
| Temperature Rise | Max. 65°C |
| Coil Voltage | See coil data table |

►COIL DATA

Single side stable                                            standard(200mW) 20°C

| Order Number | Norminal Voltage (VDC) | Pick-up voltage VDC (Max.) | Drop-out voltag VDC (Min.) | Coil resistance Ω (10%) | allowable Voltage VDC(Max.) |
| --- | --- | --- | --- | --- | --- |
| 3 | 3 | 2.30 | 0.3 | 45 | 6 |
| 5 | 5 | 3.75 | 0.5 | 125 | 10 |
| 6 | 6 | 4.50 | 0.6 | 180 | 12 |
| 9 | 9 | 6.75 | 0.9 | 405 | 18 |
| 12 | 12 | 9.00 | 1.2 | 720 | 24 |
| 15 | 15 | 11.25 | 1.5 | 1,125 | 30 |
| 24 | 24 | 18.00 | 2.4 | 2,880 | 48 |
| 48 | 48 | 36.00 | 4.8 | 11,520 | 96 |

Single side stable                                            sensitive(150mW) 20°C

| Order Number | Norminal Voltage (VDC) | Pick-up voltage VDC (Max.) | Drop-out voltag VDC (Min.) | Coil resistance Ω (10%) | allowable Voltage VDC(Max.) |
| --- | --- | --- | --- | --- | --- |
| 3H | 3 | 2.4 | 0.3 | 60 | 7.0 |
| 5H | 5 | 4.0 | 0.5 | 167 | 11.5 |
| 6H | 6 | 4.8 | 0.6 | 240 | 13.8 |
| 9H | 9 | 7.2 | 0.9 | 540 | 20.8 |
| 12H | 12 | 9.6 | 1.2 | 960 | 27.7 |
| 15H | 15 | 12.0 | 1.5 | 1,500 | 34.6 |
| 24H | 24 | 19.2 | 2.4 | 3,840 | 55.4 |

Latching (1 coil)                                              standard(100mW) 20°C

| Order Number | Norminal Voltage (VDC) | Set/Reset voltage VDC (Max.) | Coil resistance Ω (10%) | allowable Voltage VDC(Max.) |
| --- | --- | --- | --- | --- |
| 3-L1 | 3 | 2.25 | 90 | 8.4 |
| 5-L1 | 5 | 3.75 | 250 | 14 |
| 6-L1 | 6 | 4.50 | 360 | 17 |
| 9-L1 | 9 | 6.75 | 810 | 25 |
| 12-L1 | 12 | 9.00 | 1,440 | 34 |
| 15-L1 | 15 | 11.25 | 2,220 | 42 |
| 24-L1 | 24 | 18.00 | 4,000 | 56 |

Latching (2 coil)                                              standard(200mW) 20°C

| Order Number | Norminal Voltage (VDC) | Set/Reset voltage VDC (Max.) | Coil resistance Ω (10%) | allowable Voltage VDC(Max.) |
| --- | --- | --- | --- | --- |
| 3-L2 | 3 | 2.25 | 45 | 6 |
| 5-L2 | 5 | 3.75 | 125 | 10 |
| 6-L2 | 6 | 4.50 | 180 | 12 |
| 9-L2 | 9 | 6.75 | 405 | 18 |
| 12-L2 | 12 | 9.00 | 720 | 24 |
| 15-L2 | 15 | 11.25 | 1,125 | 30 |
| 24-L2 | 24 | 18.00 | 2,040 | 48 |

Latching (1 coil)                                               sensitive(75mW) 20°C

| Order Number | Norminal Voltage (VDC) | Set/Reset voltage VDC (Max.) | Coil resistance Ω (10%) | allowable Voltage VDC(Max.) |
| --- | --- | --- | --- | --- |
| 5H-L1 | 5 | 4.0 | 330 | 16 |
| 6H-L1 | 6 | 4.8 | 480 | 19 |
| 9H-L1 | 9 | 7.2 | 1,080 | 29 |
| 12H-L1 | 12 | 9.6 | 1,920 | 39 |
| 15H-L1 | 15 | 12.0 | 3,000 | 43 |
| 24H-L1 | 24 | 19.2 | 7,680 | 78 |

Latching (2 coil)                                             sensitive(150mW) 20°C

| Order Number | Norminal Voltage (VDC) | Set/Reset voltage VDC (Max.) | Coil resistance Ω (10%) | allowable Voltage VDC(Max.) |
| --- | --- | --- | --- | --- |
| 5H-L2 | 5 | 4.0 | 167 | 11.5 |
| 6H-L2 | 6 | 4.8 | 240 | 13.8 |
| 9H-L2 | 9 | 7.2 | 540 | 20.8 |
| 12H-L2 | 12 | 9.6 | 960 | 27.7 |
| 15H-L2 | 15 | 12.0 | 1,500 | 34.6 |
| 24H-L2 | 24 | 19.2 | 3,840 | 55.4 |

►SAFETY APPROVED RATING

| UL | 0.5A 60VDC 2A 25VDC, 1A 100VAC (Industrial control, business equipment) 1A 120VAC (Telephone equipment) |
| --- | --- |

►SAFETY APPROVED RATING

| Voltage | Power | Number of operations |
| --- | --- | --- |
|  |  | Resistive Load | Inductive Load(cos phi=0.7) |
| 50mV | 50μW | 5 x 107 | 5 x 107 |
| 30VDC | 20W | 3 x 106 | 1 x 106 |
| 30VDC | 30W | 1 x 106 | 3 x 1075 |
| 30VDC | 60W | 1 x 105 | 1.5 x 1074 |
| 60VDC | 20W | 3 x 106 | -- |
| 60VDC | 30W | 5 x 105 | -- |
| 60VDC | 60W | 1 x 105 | -- |
| 30VAC | 40VA | 3 x 106 | 1 x 106 |
| 30VAC | 80VA | 1 x 106 | 3 x 105 |
| 30VAC | 120VA | 1 x 105 | 1.5 x 104 |
| 60VAC | 40VA | 3 x 106 | 1 x 106 |
| 60VAC | 80VA | 1 x 106 | 3 x 105 |
| 60VAC | 120VA | 1 x 105 | 1.5 x 104 |
| 125VAC | 40VA | 3 x 106 | 1 x 106 |
| 125VAC | 80VA | 1 x 106 | 3 x 105 |
| 125VAC | 125VA | 1 x 105 | 1.55 x 104 |

►ORDERING INFORMATION

►DIMENSIONS  (Unit: mm)

►CHARACTERISTICS CURVE

# Text boxes

#### BC4